## Slide 1: CSE 424 Computer Architecture Chapter 2: Instructions: Language of the Computer (focus on MIPS ISA – Appendix A)
Adwait Jog (http://adwaitjog.github.io/)
Based on the slides from Mary. J. Irwin (Penn State)
[Adapted from Computer Organization and Design,
5th Edition, Patterson & Hennessy,
Morgan Kaufmann]
Notes: Combinations to AV system, etc. 0812
Call AV hot line at 8-777-0035

## Slide 2: Review: The Execute Cycle
Processor
Control
Datapath
Memory
contents Reg #4 ADD contents Reg #2
results put in Reg #2
The datapath executes the instructions as directed by control
000000 00100 00010 0001000000100000
Memory stores both instructions and data
Devices
Input
Output
Network

## Slide 3: Review: Processor Organization
Control needs to have circuitry to
  Decide which is the next instruction and fetch it from memory
  Decode the instruction
  Issue signals that control the way information flows between datapath components
  Control what operations the datapath’s functional units perform
  Execute instructions - functional units (e.g., adder) and storage locations (e.g., register file)
  Interconnect the functional units so that the instructions can be executed as required
  Load data from and store data to memory
Datapath needs to have circuitry to
Fetch
Decode
Exec
Notes: For lecture

## Slide 4: Two Key Principles of Machine Design
  Instructions are represented as numbers and, as such, are indistinguishable from data
  Programs are stored in alterable memory (that can be read or written to) just like data
Stored-program (von Neumann) concept
  Programs can be shipped as files of binary numbers – binary compatibility
  Computers can inherit ready-made software provided they are compatible with an existing ISA – leads industry to align around a small number of ISAs
Accounting prg (machine code)
C compiler (machine code)
Payroll data
Source code in C for Acct program
Memory

## Slide 5: Assembly Language Instructions
The language of the machine
  Want an ISA that makes it easy to build the hardware and the compiler (whose job it is to translate programs written in a high level language (like C) to assembly code) while maximizing performance and minimizing cost
Our target: the MIPS ISA
  similar to other ISAs developed since the 1980's
  used by Broadcom, Cisco, NEC, Nintendo, Sony, …
Design goals: maximize performance, minimize cost, reduce design time (time-to-market), minimize power consumption, maximize reliability

## Slide 6: RISC - Reduced Instruction Set Computer
RISC philosophy
  fixed instruction lengths
  load-store instruction sets
  limited number of addressing modes
  limited number of operations
MIPS, Sun SPARC, HP PA-RISC, IBM PowerPC …
Instruction sets are measured by how well compilers can use them as opposed to how well assembly language programmers can use them
CISC (C for complex), e.g., Intel x86
Notes: As opposed to CISC – Complicated Instruction Set Architecture (ala the x86)

## Slide 7: The Four RISC Design Principles
Simplicity favors regularity.
Smaller is faster.
Make the common case fast.
Good design demands good compromises.
Notes: Write these on the board.

## Slide 8: MIPS (RISC) Design Principles
Simplicity favors regularity
  fixed size instructions
  small number of instruction formats
  opcode always the first 6 bits
Smaller is faster
  limited instruction set
  limited number of registers in register file
  limited number of addressing modes
Make the common case fast
  arithmetic operands from the register file (load-store machine)
  allow instructions to contain immediate operands
Good design demands good compromises
  three instruction formats
Notes: Leave in hide mode …

## Slide 9: MIPS Arithmetic Instruction
MIPS assembly language arithmetic statement
add $t0, $s1, $s2
sub $t0, $s1, $s2
Each arithmetic instruction performs only one operation
Each arithmetic instruction specifies exactly three operands
  destination  source1 op source2
  Operand order is fixed (the destination is specified first)
The operands are contained in the datapath’s register file ($t0, $s1, $s2)
Notes: For class handout

## Slide 10: MIPS Arithmetic Instruction
MIPS assembly language arithmetic statement
add $t0, $s1, $s2
sub $t0, $s1, $s2
Each arithmetic instruction performs only one operation
Each arithmetic instruction specifies exactly three operands
  destination  source1 op source2
  Operand order is fixed (the destination is specified first)
The operands are contained in the datapath’s register file ($t0, $s1, $s2)
Notes: For lecture

## Slide 11: Compiling More Complex Statements
Assuming variable b is stored in register $s1, c is stored in $s2, and d is stored in $s3 and the result is to be left in $s0, what is the assembler equivalent to the C statement
h = (b - c) + d
Notes: For class handout

## Slide 12: Compiling More Complex Statements
Assuming variable b is stored in register $s1, c is stored in $s2, and d is stored in $s3 and the result is to be left in $s0, what is the assembler equivalent to the C statement
h = (b - c) + d
sub $t0, $s1, $s2
add $s0, $t0, $s3
Notes: For lecture
sub $t0, $s1, $s2
add $s0, $t0, $s3

## Slide 13: MIPS Register File
Operands of arithmetic instructions must be from a limited number of special locations contained in the datapath’s register file
  Thirty-two 32-bit registers
    Two read ports
    One write port
Registers are
  Faster than main memory
    Smaller is faster & Make the common case fast
  Easy for a compiler to use
    e.g., (A*B) – (C*D) – (E*F) can do multiplies in any order
  Improves code density
    Since register are named with fewer bits than a memory location
Register addresses are indicated by using $
Notes: For class handout

## Slide 14: MIPS Register File
Operands of arithmetic instructions must be from a limited number of special locations contained in the datapath’s register file
  Thirty-two 32-bit registers
    Two read ports
    One write port
write
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
locations
Register File
32
5
32
5
5
32
Registers are
  Faster than main memory
    Smaller is faster & Make the common case fast
  Easy for a compiler to use
    e.g., (A*B) – (C*D) – (E*F) can do multiplies in any order
  Improves code density
    Since register are named with fewer bits than a memory location
Register addresses are indicated by using $
25 =
Notes: For lecture
All machines (since 1975) have used general purpose registers
How many bits wide are each of the lines going into/out of the register file?

## Slide 15: MIPS Arithmetic Instructions
MIPS assembly language arithmetic statements
  dst  src1 op src2
add $t0, $s1, $s2
sub $t0, $s1, $s2
The operands ($t0, $s1, $s2) are contained in the datapath’s register file which contains thirty-two 32-bit registers
  Two read ports
  One write port
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
locations
write

## Slide 16: MIPS Register Naming Convention
Nick Name | Register Number | Usage
$zero | 0 | constant 0 (hardware)
$at | 1 | reserved for assembler
$v0 - $v1 | 2-3 | returned values
$a0 - $a3 | 4-7 | arguments
$t0 - $t7 | 8-15 | temporaries
$s0 - $s7 | 16-23 | saved values
$t8 - $t9 | 24-25 | temporaries
$k0 - $k1 | 26-27 | reserved for OS
$gp | 28 | global pointer
$sp | 29 | stack pointer
$fp | 30 | frame pointer
$ra | 31 | return addr (hardware)

## Slide 17: Registers vs. Memory
Arithmetic instructions operands must be in registers
  But only thirty-two registers are provided
The compiler associates variables with registers
What about programs with lots of variables?
Processor
Control
Datapath
Memory
Devices
Input
Output
Network
Notes: For class handout

## Slide 18: Registers vs. Memory
Arithmetic instructions operands must be in registers
  But only thirty-two registers are provided
The compiler associates variables with registers
Processor
Control
Datapath
Memory
Devices
Input
Output
Network
What about programs with lots of variables?
Notes: For lecture
Store variables in memory!
So have to be able to move variables to/from memory and the register file easily

## Slide 19: Registers vs. Memory
Registers are faster to access than memory.
There are not as many registers as variables (in most programs).
Sometimes, the variables are arrays or structs or objects, and they won’t fit into one register.
Operating on memory-resident data requires loads and stores.
  This is still true even if the ISA allows memory operands; in this case, the loads and stores are implicit in the instruction design.
So, keep as much data as you can in the registers, and keep the rest in memory.
Better, keep the most-frequently-used data in registers for as long as possible.
Only “spill to memory” when there is too much data to hold in the registers all at once.
  “spill to memory” = “copy a register value to memory, to allow the register to be used for another purpose”
Compiler register allocation and optimization is important.

## Slide 20: Processor – Memory Interconnections
Memory is a large, single-dimensional array
A memory address acts as the index into the memory array
Processor
Memory
32 bits
?
locations
read addr/
write addr
read data
write data
1111 …1
1011 … 1
1001 … 0
read/write
control
Notes: For class handout

## Slide 21: Processor – Memory Interconnections
Memory is a large, single-dimensional array
A memory address acts as the index into the memory array
Processor
Memory
32 bits
?
locations
read addr/
write addr
read data
write data
32
32
32
232 Bytes (4 GB)  230 Words (1 GW)
= 4 Bytes = 1 Word
0
4
8
The data stored in the memory
The word address of the data
1111 …1
1011 … 1
1001 … 0
read/write
control
Notes: For lecture
How many bits per line?

## Slide 22: Word Addresses vs Byte Addresses
  Alignment restriction - the memory address of a word must be on natural word boundaries (a multiple of 4 in MIPS-32)
  But since 8-bit bytes are so useful, most architectures also support addressing individual bytes in memory
Big Endian: leftmost byte is word address
    IBM 360/370, Motorola 68k, MIPS, Sparc, HP PA
Little Endian: rightmost byte is word address
    Intel 80x86, DEC Vax, DEC Alpha (Windows NT)
msb
lsb
3 2 1 0
little endian byte 0
0 1 2 3
big endian byte 0
Notes: Talk about the reasons (performance) for the word/byte alignment restriction

## Slide 23: Accessing Memory
MIPS has two basic data transfer instructions for accessing memory (assume $s3 holds 2410)
lw $t0, 4($s3) #load word from memory
sw $t0, 8($s3) #store word to memory
The data transfer instruction must specify
  where in memory to read from (load) or write to (store) – memory address
  where in the register file to write to (load) or read from (store) – register destination (source)
The memory address is formed by summing the constant portion of the instruction and the contents of the second register
Notes: For class handout

## Slide 24: Accessing Memory
MIPS has two basic data transfer instructions for accessing memory (assume $s3 holds 2410)
lw $t0, 4($s3) #load word from memory
sw $t0, 8($s3) #store word to memory
The data transfer instruction must specify
  where in memory to read from (load) or write to (store) – memory address
  where in the register file to write to (load) or read from (store) – register destination (source)
The memory address is formed by summing the constant portion of the instruction and the contents of the second register
2810
3210
Notes: For lecture
What is the memory address of the given load and store instructions if $s3 contains the address 24?

## Slide 25: MIPS Memory Addressing
The memory address is formed by summing the constant portion of the instruction and the contents of the second (base) register
lw $t0, 4($s3) #what? is loaded into $t0
sw $t0, 8($s3) #$t0 is stored where?
Memory
. . . 0 1 0 0
Data
Word Address
0
4
8
12
16
20
24
. . . 1 0 0 0
. . . 0 0 1 0
. . . 0 0 0 1
. . . 1 1 0 0
. . . 0 1 0 1
. . . 0 1 1 0
$s3 holds 8
Notes: For class handout

## Slide 26: MIPS Memory Addressing
The memory address is formed by summing the constant portion of the instruction and the contents of the second (base) register
lw $t0, 4($s3) #what? is loaded into $t0
sw $t0, 8($s3) #$t0 is stored where?
Memory
. . . 0 1 0 0
32 bit Data
Word Address
0
4
8
12
16
20
24
. . . 1 0 0 0
. . . 0 0 1 0
. . . 0 0 0 1
. . . 1 1 0 0
. . . 0 1 0 1
. . . 0 1 1 0
$s3 holds 8
in memory location 16
. . . 0001
. . . 0001
Notes: For lecture

## Slide 27: Compiling with Loads and Stores
Assuming variable b is stored in $s2 and that the base address of array A is in $s3, what is the three statement MIPS assembly code for the C statement
A[8] = A[2] - b
$s3
$s3+4
$s3+8
$s3+12
. . .
A[2]
A[3]
. . .
A[1]
A[0]
Notes: For class handout

## Slide 28: Compiling with Loads and Stores
Assuming variable b is stored in $s2 and that the base address of array A is in $s3, what is the three statement MIPS assembly code for the C statement
A[8] = A[2] - b
$s3
$s3+4
$s3+8
$s3+12
. . .
A[2]
A[3]
. . .
A[1]
A[0]
lw $t0, 8($s3)
sub $t0, $t0, $s2
sw $t0, 32($s3)
Notes: For lecture
lw $t0, 8($s3)
sub $t0, $t0, $s2
sw $t0, 32($s3)

## Slide 29: Compiling with a Variable Array Index
Assuming that the base address of array A is in register $s4, and variables b, c, and i are in $s1, $s2, and $s3, respectively, complete the MIPS assembly code for the C statement
c = A[i] - b
add $t1, $s3, $s3 #array index i is in $s3
add $t1, $t1, $t1 #temp reg $t1 holds 4*i
$s4
$s4+4
$s4+8
$s4+12
. . .
A[2]
A[3]
. . .
A[1]
A[0]
Notes: For class handout

## Slide 30: Compiling with a Variable Array Index
Assuming that the base address of array A is in register $s4, and variables b, c, and i are in $s1, $s2, and $s3, respectively, complete the MIPS assembly code for the C statement
c = A[i] - b
add $t1, $s3, $s3 #array index i is in $s3
add $t1, $t1, $t1 #temp reg $t1 holds 4*i
$s4
$s4+4
$s4+8
$s4+12
. . .
A[2]
A[3]
. . .
A[1]
A[0]
add $t1, $t1, $s4 #addr of A[i] now in $t1
lw $t0, 0($t1)
sub $s2, $t0, $s1
Notes: For class handout
We add i 4 times so that we know the displacement value (iX4) to add with the Base address.

## Slide 31: Address Calculation – One-Dimensional Array
int A[10];
  or, in C, int *A = malloc(10*sizeof(int));
The compiler, linker, loader (if A is global), or runtime stack management (if A is local), or runtime heap management (if A is dynamically-allocated), cooperate to place A into memory, in consecutive locations.
A[0] is at the lowest address of the array elements.
Address of A[i] = address of A[0] + i × size of one int
If i is a constant expression, the compiler precomputes the proper offset, and uses it in an lw instruction.
If i is not known until runtime, the compiler generates code to compute the offset, adds it to the base address, and uses an lw instruction with 0 offset.

## Slide 32: Dealing with Constants
Small constants are used quite frequently (50% of operands in many common programs)
  e.g., A = A + 5; B = B + 1; C = C - 18;
Solutions? Why not?
  Create hard-wired registers (like $zero) for constants like 1, 2, 4, 10, …
  Put “typical constants” in memory and load them
  . . .
How do we make this work? How do we Make the common case fast !
Notes: in gcc 52% of arithmetic operations involve constants – in spice its 69%
have the students answer why not – speed and limited number of registers

## Slide 33: Constant (or Immediate) Operands
Include constants inside arithmetic instructions
  Much faster than if they have to be loaded from memory (they come in from memory with the instruction itself)
MIPS immediate instructions
addi $s3, $s3, 4 #$s3 = $s3 + 4
And to move (copy) the contents of one register to another in one instruction
There is no subi instruction, can you guess why not?
Notes: For class handout
There is no subi because MIPS can use negative constants for addi in stead of having an extra instruction.

## Slide 34: Constant (or Immediate) Operands
Include constants inside arithmetic instructions
  Much faster than if they have to be loaded from memory (they come in from memory with the instruction itself)
MIPS immediate instructions
addi $s3, $s3, 4 #$s3 = $s3 + 4
And to move (copy) the contents of one register to another in one instruction
There is no subi instruction, can you guess why not?
add $s4, $s3, $zero
Notes: For lecture
much faster than if loaded from memory
addi (and slti) does sign extend of immediate operand into the leftmost bits of the destination register (ie., copies the leftmost bit of the 16-bit immediate value into the upper 16 bits)
by contrast, ori and andi loads zero’s into the upper 16 bits and so is usually used (instead of the addi) to build 32 bit constants
MIPS supports –ve constants; so need for Subi instruction

## Slide 35: MIPS Instructions, so far
Category | Instr | Example | Meaning
Arithmetic | add | add $s1, $s2, $s3 | $s1 = $s2 + $s3
 | subtract | sub $s1, $s2, $s3 | $s1 = $s2 - $s3
 | add immediate | addi $s1, $s2, 4 | $s1 = $s2 + 4
Data transfer | load word | lw $s1, 32($s2) | $s1 = Memory($s2+32)
 | store word | sw $s1, 32($s2) | Memory($s2+32) = $s1
Notes: similarity of the binary representation of related instructions simplifies the hardware design

## Slide 36: MIPS Organization, so far
Processor
Memory
32 bits
230
words
=
232
Bytes
(4 GB)
read/write
addr
read data
write data
word address
(binary)
0…0000
0…0100
0…1000
0…1100
1…1100
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
registers
($zero - $ra)
32
32
32
32
32
32
5
5
5
ALU
32
32
32
0
1
2
3
7
6
5
4
byte address
(big Endian)
Arithmetic instructions – to/from the register file
Load/store instructions – to/from memory
Notes: Notice least two significant bits of the (word) address are always zero

## Slide 37: Unsigned Binary Representation
Hex | Binary | Decimal
0x00000000 | 0…0000 | 0
0x00000001 | 0…0001 | 1
0x00000002 | 0…0010 | 2
0x00000003 | 0…0011 | 3
0x00000004 | 0…0100 | 4
0x00000005 | 0…0101 | 5
0x00000006 | 0…0110 | 6
0x00000007 | 0…0111 | 7
0x00000008 | 0…1000 | 8
0x00000009 | 0…1001 | 9
 | … | 
0xFFFFFFFC | 1…1100 | 
0xFFFFFFFD | 1…1101 | 
0xFFFFFFFE | 1…1110 | 
0xFFFFFFFF | 1…1111 | 
232 - 1
232 - 2
232 - 3
232 - 4
232 - 1
1 1 1 . . . 1 1 1 1 bit
31 30 29 . . . 3 2 1 0 bit position
231 230 229 . . . 23 22 21 20 bit weight
1 0 0 0 . . . 0 0 0 0 - 1
Notes: All positive numbers - no sign bit
0x before a number implies Hexadecimal representation.
last entry is most significant byte address
fourth from last entry is most significant word address

## Slide 38: Signed Binary Representation
2’sc binary | decimal
1000 | -8
1001 | -7
1010 | -6
1011 | -5
1100 | -4
1101 | -3
1110 | -2
1111 | -1
0000 | 0
0001 | 1
0010 | 2
0011 | 3
0100 | 4
0101 | 5
0110 | 6
0111 | 7
23 - 1 =
-(23 - 1) =
-23 =
1010
complement all the bits
1011
and add a 1
complement all the bits
0101
and add a 1
0110
two’s complement negation
Notes: PH Sec. 2.4
Signed numbers – assuming 2’s complement representation – for eight bits
Note that msb of 1 indicates a negative number, the bit string all 0’s is zero, that the largest positive number that can be represented is 7 (2**(n-1) –1 for n bits) whereas the largest negative number that can be represented is –8 (-2**(n-1) for n bits)
Also note that the negation of -8 is -8, and 7 + 1 is -8, due to overflow.

## Slide 39: Signed Binary Representation
Hex | Binary | Decimal
0x00000000 | 0…0000 | 0
0x00000001 | 0…0001 | 1
0x00000002 | 0…0010 | 2
0x00000003 | 0…0011 | 3
0x00000004 | 0…0100 | 4
0x00000005 | 0…0101 | 5
0x00000006 | 0…0110 | 6
0x00000007 | 0…0111 | 7
0x00000008 | 0…1000 | 8
0x00000009 | 0…1001 | 9
 | … | 
0xFFFFFFFC | 1…1100 | -4
0xFFFFFFFD | 1…1101 | -3
0xFFFFFFFE | 1…1110 | -2
0xFFFFFFFF | 1…1111 | -1
−231 to (231 − 1)
1 1 1 . . . 1 1 1 1 bit
31 30 29 . . . 3 2 1 0 bit position
-231 230 229 . . . 23 22 21 20 bit weight
(−) 1 0 0 . . . 0 0 0 0
(+) 0 1 1 . . . 1 1 1 1
two’s complement
n bits, the range is −2n-1 to (2n-1 − 1)
Notes: PH Sec. 2.4
Exercise:
What is the most-negative 4-bit value? 1000
most-positive? 0111
one plus most-positive? 0001 + 0111 = 1000 (overflow)

## Slide 40: Zero Extension, Sign Extension
Represent a number using more bits, but preserve the numeric value
  unsigned – use zero-extension
    4 bits to 8 bits, wxyz => 0000wxyz
  signed – use sign-extension
    4 bits to 8 bits, wxyz => wwwwwxyz
    replicate the left-most bit
  Exercise: prove that this works as claimed
Notes: PH Sec. 2.4

## Slide 41: Hex to Binary and Back
Hex | Binary | Hex | Binary | Hex | Binary | Hex | Binary
0hex | 0000two | 4hex | 0100two | 8hex | 1000two | chex | 1100two
1hex | 0001two | 5hex | 0101two | 9hex | 1001two | dhex | 1101two
2hex | 0010two | 6hex | 0110two | ahex | 1010two | ehex | 1110two
3hex | 0011two | 7hex | 0111two | bhex | 1011two | fhex | 1111two
eca8 6420hex
0001 0011 0101 0111 1001 1011 1101 1111two
Notes: Class handout

## Slide 42: Binary to Hex and Back
Hex | Binary | Hex | Binary | Hex | Binary | Hex | Binary
0hex | 0000two | 4hex | 0100two | 8hex | 1000two | chex | 1100two
1hex | 0001two | 5hex | 0101two | 9hex | 1001two | dhex | 1101two
2hex | 0010two | 6hex | 0110two | ahex | 1010two | ehex | 1110two
3hex | 0011two | 7hex | 0111two | bhex | 1011two | fhex | 1111two
eca8 6420hex
0001 0011 0101 0111 1001 1011 1101 1111two
1110 1100 1010 1000 0110 0100 0010 0000two
1357 9bdfhex
= 0x1357 9bdf
Notes: For lecture

## Slide 43: Machine Language - Arithmetic Instruction
Instructions, like registers and words of data, are also 32 bits long
  Example: add $t0, $s1, $s2
  registers have numbers $t0=8,$s1=17,$s2=18
Instruction Format:
Can you guess what the field names stand for?
op rs rt rd shamt funct
000000 10001 10010 01000 00000 100000
Notes: For class handout

## Slide 44: Machine Language - Arithmetic Instruction
Instructions, like registers and words of data, are also 32 bits long
  Example: add $t0, $s1, $s2
  registers have numbers $t0=8,$s1=17,$s2=18
Instruction Format (R-Type):
op rs rt rd shamt funct
000000 10001 10010 01000 00000 100000
Can you guess what the field names stand for?
0x00 17 18 8 0 0x20
Notes: For lecture
Shows instruction in both binary and decimal/hex formats

## Slide 45: MIPS Instruction Fields
op
rs
rt
rd
shamt
funct
op rs rt rd shamt funct
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
= 32 bits
Notes: for class handout

## Slide 46: MIPS Instruction Fields
op
rs
rt
rd
shamt
funct
op rs rt rd shamt funct
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
= 32 bits
opcode indicating operation to be performed
register file address of the first source operand
register file address of the second source operand
register file address of the result’s destination
shift amount (for shift instructions)
function code that selects the specific variant of the operation specified in the opcode field
Notes: for lecture