## Slide 1: CSE 424 Computer Architecture MIPS ISA (contd.)
Adwait Jog (http://adwaitjog.github.io/)
Based on the slides from Mary. J. Irwin (Penn State)
[Adapted from Computer Organization and Design,
5th Edition, Patterson & Hennessy,
Morgan Kaufmann]

## Slide 2: MIPS Instruction Fields
op
rs
rt
rd
shamt
funct
op rs rt rd shamt funct
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
= 32 bits
opcode indicating operation to be performed
register file address of the first source operand
register file address of the second source operand
register file address of the result’s destination
shift amount (for shift instructions)
function code that selects the specific variant of the operation specified in the opcode field
Notes: for lecture

## Slide 3: Machine Language - Load Instruction
Consider the load-word and store-word instr’s
  What would the regularity principle have us do?
    But . . . Good design demands compromise
Introduce a new type of instruction format
  I-type for data transfer instructions (previous format was R-type for register)
Example: lw $t0, 24($s2)
Where's the compromise?
op rs rt 16 bit number
0x23 18 8 2410
100011 10010 01000 0000000000011000
Notes: For class handout

## Slide 4: Machine Language - Load Instruction
Consider the load-word and store-word instr’s
  What would the regularity principle have us do?
    But . . . Good design demands compromise
Introduce a new type of instruction format
  I-type for data transfer instructions (previous format was R-type for register)
Example: lw $t0, 24($s2)
op rs rt 16 bit number
0x23 18 8 2410
100011 10010 01000 0000000000011000
Where's the compromise?
Notes: For lecture
destination address no longer in the rd field - now in the rt field
offset limited to 16 bits - so can’t get to every location in memory (with a fixed base address)

## Slide 5: Memory Address Location
Example: lw $t0, 24($s2)
Memory
data
word address (hex)
0x00000000
0x00000004
0x00000008
0x0000000c
0xf f f f f f f f
$s2
0x12004094
0x00000002
2410 + $s2 =
Notes: For class handout

## Slide 6: Memory Address Location
Example: lw $t0, 24($s2)
Memory
data
word address (hex)
0x00000000
0x00000004
0x00000008
0x0000000c
0xf f f f f f f f
$s2
0x12004094
0x00000002
2410 + $s2 =
Note that the offset can be positive or negative
. . . 0001 1000
+ . . . 1001 0100
. . . 1010 1100 =
0x120040ac
0x120040ac
$t0
Notes: For lecture
What is the address of the memory location that gets loaded into $t0?
…10010100
…00011000
--------------
…10101100= 0x020040ac
In SPIM, the code starts at 0x0040 0000 and the data area at 0x1000 0000 and the stack area at 0x7fff de00

## Slide 7: Machine Language - Store Instruction
Example: sw $t0, 24($s2)
A 16-bit offset means access is limited to memory locations within a range of +213-1 to -213 (~8,192) words (+215-1 to -215 (~32,768) bytes) of the address in the base register $s2
  2’s complement (1 sign bit + 15 magnitude bits)
op rs rt 16 bit number
0x2b 18 8 2410
101011 10010 01000 0000000000011000
Notes: For class handout

## Slide 8: Machine Language - Store Instruction
Example: sw $t0, 24($s2)
A 16-bit offset means access is limited to memory locations within a range of +213-1 to -213 (~8,192) words (+215-1 to -215 (~32,768) bytes) of the address in the base register $s2
  2’s complement (1 sign bit + 15 magnitude bits)
op rs rt 16 bit number
0x2b 18 8 2410
101011 10010 01000 0000000000011000
Notes: For lecture
why is it 2**13 (2**15) and NOT 2**14 (2**16) like we just saw with memory (here we have to represent signed numbers so the most significant bit is the sign bit)

## Slide 9: Machine Language – Immediate Instructions
What instruction format is used for the addi ? addi $s3, $s3, 4 #$s3 = $s3 + 4
Machine format:
op rs rt 16 bit immediate
I format
8 19 19 4
The constant is kept inside the instruction itself!
  So must use the I format – Immediate format
  Limits immediate values to the range +215–1 to -215
0x08 19 19 4
Notes: For lecture
addi and slti does sign extend of immediate operand into the leftmost bits of the destination register (ie., copies the leftmost bit of the 16-bit immediate value into the upper 16 bits)
by contrast, ori and andi loads zero’s into the upper 16 bits and so is usually used (instead of the addi) to build 32 bit constants

## Slide 10: Machine Language – Immediate Instructions
What instruction format is used for the addi ? addi $s3, $s3, 4 #$s3 = $s3 + 4
Machine format:
op rs rt 16 bit immediate
I format
8 19 19 4
The constant is kept inside the instruction itself!
  So must use the I format – Immediate format
  Limits immediate values to the range +215–1 to -215
0x08 19 19 4
Notes: For lecture
addi and slti does sign extend of immediate operand into the leftmost bits of the destination register (ie., copies the leftmost bit of the 16-bit immediate value into the upper 16 bits)
by contrast, ori and andi loads zero’s into the upper 16 bits and so is usually used (instead of the addi) to build 32 bit constants

## Slide 11: Instruction Format Encoding, so far
Can reduce the complexity with multiple formats by keeping them as similar as possible
  First three fields are the same in R-type and I-type
Each format has a distinct set of values in the op field
Instr | Frmt | op | rs | rt | rd | shamt | funct | address
add | R | 0 | reg | reg | reg | 0 | 32ten | NA
sub | R | 0 | reg | reg | reg | 0 | 34ten | NA
addi | I | 8ten | reg | reg | NA | NA | NA | constant
lw | I | 35ten | reg | reg | NA | NA | NA | address
sw | I | 43ten | reg | reg | NA | NA | NA | address

## Slide 12: Assembling Code
Remember the assembler code we compiled last lecture for the C statement
A[8] = A[2] - b
lw $t0, 8($s3) #load A[2] into $t0
sub $t0, $t0, $s2 #subtract b from A[2]
sw $t0, 32($s3) #store result in A[8]
Assemble the MIPS object code for these three instructions (in decimal is fine)
lw
sw
sub
Notes: For class handout

## Slide 13: Assembling Code
Remember the assembler code we compiled last lecture for the C statement
A[8] = A[2] - b
lw $t0, 8($s3) #load A[2] into $t0
sub $t0, $t0, $s2 #subtract b from A[2]
sw $t0, 32($s3) #store result in A[8]
Assemble the MIPS object code for these three instructions (in decimal is fine)
35
lw
19
8
8
43
sw
19
8
32
0
sub
8
18
8
0
34
Notes: For lecture
lw 35 19 8 8
sub 0 8 18 8 0 34
sw 43 19 8 32

## Slide 14: Review: MIPS Instructions, so far
Category | Instr | Op Code | Example | Meaning
Arithmetic (R format) | add | 0 & 20hex | add $s1, $s2, $s3 | $s1 = $s2 + $s3
 | subtract | 0 & 22hex | sub $s1, $s2, $s3 | $s1 = $s2 - $s3
Arithmetic (I format) | add immediate | 8hex | addi $s1, $s2, 4 | $s1 = $s2 + 4
Data transfer (I format) | load word | 23hex | lw $s1, 100($s2) | $s1 = Memory($s2+100)
 | store word | 2bhex | sw $s1, 100($s2) | Memory($s2+100) = $s1
Notes: similarity of the binary representation of related instructions simplifies the hardware design

## Slide 15: Review: Addressing Modes, so far
1. Register addressing
op rs rt rd funct
Register
word operand
3. Immediate addressing
op rs rt operand
op rs rt offset
2. Base (displacement) addressing
base register
Memory
word or byte operand

## Slide 16: MIPS32 ISA
Instruction Categories
  Computational
  Load/Store
  Jump and Branch
  Floating Point
    coprocessor
  Memory Management
  Special
R0 - R31
PC
HI
LO
Registers
op
op
op
rs
rt
rd
sa
funct
rs
rt
immediate
jump target
3 Instruction Formats: all 32 bits wide
R format
I format
J format

## Slide 17: Representing Instructions in the Machine
Arithmetic instructions
op rs rt rd shamt funct
6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
add $t0, $s1, $s2
000000 10001 10010 01000 00000 100000
0x00 17 18 8 0 0x20
sub $t0, $s1, $s2
000000 10001 10010 01000 00000 100010
0x00 17 18 8 0 0x22
Remember the MIPS-32 instruction fields, R format

## Slide 18: Representing Instructions in the Machine
Data transfer instructions
6 bits 5 bits 5 bits 16 bit
lw $t0, 24($s2)
sw $t0, 24($s2)
Remember the MIPS-32 instruction fields, I format
op rs rt two’s compl number
0x23 18 8 24ten
100011 10010 01000 0000000000011000
101011 10010 01000 0000000000011000
0x2B 18 8 24ten

## Slide 19: Representing Instructions in the Machine
A 16-bit offset means, for loads and stores, that access is limited to memory locations within a range of +213 - 1 to -213 (~8,192) words (+215 - 1 to -215 (~32,768) bytes) of the address in the base register
  two’s complement (1 sign bit + 15 magnitude bits)
And limits immediate values to the range +215 - 1 to -215
Immediate instructions
addi $t0, $s2, 4
001000 10010 01000 0000000000000100
0x08 18 8 4ten

## Slide 20: Assemble these … (in hex)
add $t0, $s3, $zero
sub $t0, $s3, $s2
addi $t0, $s3, -16
lw $t0, 257($zero)
sw $t0, -24($s3)
Notes: For class handout

## Slide 21: Assemble these … (in hex)
add $t0, $s3, $zero
sub $t0, $s3, $s2
addi $t0, $s3, -16
lw $t0, 257($zero)
sw $t0, -24($s3)
0x00 19 18 8 0 0x22
0x00 19 0 8 0 0x20
0x08 19 8 0xFFF0
0x23 0 8 0x0101
0x2B 19 8 0xFFE8
Notes: For lecture
The add moves $s3 contents into $t0
-16 = 0…010000 = 1…10 1111+1 = 1…11 0000
257 = 0…01 0000 0001
Point out that this is the way to specify an absolute address in the MIPS ISA – i.e., by using register 0 as the base register. Also mention that 0($s3) means no displacement off of the base register.
-24 = 0…011000 = 1…1100111+1 = 1… 1110 1000

## Slide 22: MIPS-32 Shift Operations
Shifts move all the bits in a word left or right by a specified amount
sll $t2, $s0, 8 #$t2 = $s0 << 8 bits
srl $t2, $s0, 8 #$t2 = $s0 >> 8 bits
Instruction Format (R format)
Such shifts are called logical (notice the trailing lin the op mnemonic) because they fill with zeros
The 5-bit shamt field is just large enough to specify a value which can shift a 32-bit value 31 bit positions
0x00 16 10 8 0x00
op rs rt rd shamt funct
R format
0x00 16 10 8 0x02
sll
srl
Notes: also have sllv, srlv, and srav

## Slide 23: One More Shift Operation
An arithmetic shift (sra) must maintain the arithmetic correctness of the shifted value (i.e., a number shifted right one bit should be ½ of its original value; a number shifted left one bit should be 2 times its original value)
  sra copies the MSB bit (sign bit) as the bit shifted in
  srl shifts in zeros to the MSB
  sll shifts in zeros to the LSB so it also works for arithmetic left shifts for two’s complement (so there is no need for a sla)
sra $t2, $s0, 8 #$t2 = $s0 >> 8 bits
op rs rt rd shamt funct
0x00 16 10 8 0x03
R format

## Slide 24: Shift Examples and Decimal Equivalents
Consider shifting the value 6 = 00 … 00110two
  One bit to the left (so sll)
  One bit to the right, arithmetic (so sra)
  One bit to the right, logical (so srl)
Now consider shifting the value -6 = 11 …11010two
  One bit to the left (so sll)
  One bit to the right, arithmetic (so sra)
  One bit to the right, logical (so srl)
Notes: For class handout

## Slide 25: Shift Examples and Decimal Equivalents
Consider shifting the value 6ten = 00 … 0 0110two
  One bit to the left (so sll)
  One bit to the right, arithmetic (so sra)
  One bit to the right, logical (so srl)
Now consider shifting the value -6 = 11 …1 1010two
  One bit to the left (so sll)
  One bit to the right, arithmetic (so sra)
  One bit to the right, logical (so srl)
00 … 0 1100two
= 12ten
00 … 0 0011two
= 3ten
00 … 0 0011two
= 3ten
11 … 1 0100two
= -12ten
11 … 1 1101two
= -3ten
01 … 1 1101two
Notes: For lecture

## Slide 26: MIPS Multiply Instruction
Multiply (mult and multu) produces a double precision product
Multu (multiply unsigned) produces unsigned product while mult produces signed product
mult $s0, $s1 # hi||lo = $s0 * $s1
  Low-order word of the product is left in processor register lo and the high-order word is left in register hi
  Instructions mfhi rd and mflo rd are provided to move the product to (user accessible) registers in the register file
0 16 17 0 0 0x18

## Slide 27: MIPS Multiply Instruction
What happens with mixed-sign operands and multiplication?
Notes
  It’s a mistake to consider hi and lo separately
  The sign bit of the result is not contained in lo when the result is large enough in magnitude
t0 | t1 | hi (upper bits) | lo (lower bits)
10 | 3 | 0 | 30
-10 | 3 | -1 | -30
10 | -3 | -1 | -30
-10 | -3 | 0 | 30

## Slide 28: MIPS Divide Instruction
Divide (div and divu) generates the reminder in hi and the quotient in lo
div $s0, $s1 # lo = $s0 / $s1
# hi = $s0 mod $s1
  Instructions mfhi rd and mflo rd are provided to move the quotient and reminder to (user accessible) registers in the register file
0 16 17 0 0 0x1A

## Slide 29: MIPS Divide Instruction
What happens with mixed-sign operands and division? Let’s try div $t0, $t1 with MARS
Notes
  lo × t1 + hi is always t0
  the sign of lo is as expected
  but hi could be positive or negative
t0 | t1 | lo (quotient) | hi (remainder)
10 | 3 | 3 | 1
-10 | 3 | -3 | -1
10 | -3 | -3 | 1
-10 | -3 | 3 | -1

## Slide 30: MIPS Logical Operations
There are also a number of bit-wise logical operations in the MIPS-32 ISA
and $t0, $t1, $t2 #$t0 = $t1 & $t2
or $t0, $t1, $t2 #$t0 = $t1 | $t2
nor $t0, $t1, $t2 #$t0 = ~($t1 | $t2)
Instruction Format (R format)
andi $t0, $t1, 0xff00 #$t0 = $t1 & ff00
ori $t0, $t1, 0xff00 #$t0 = $t1 | ff00
Instruction Format (I format)
0x00 9 10 8 0 0x24
0x0C 9 8 0xFF00
and
andi

## Slide 31: Logical Operations in Action
Logical operations operate on individual bits of the operand.
  $t2 = 0…0 0000 1101 0000
  $t1 = 0…0 0011 1100 0000
and $t0, $t1, $t2 $t0 =
or $t0, $t1 $t2 $t0 =
nor $t0, $t1, $t2 $t0 =
xor $t0, $t1, $t2 $t0 =
Notes: For class handout

## Slide 32: Logic Operations in Action
Logic operations operate on individual bits of the operand.
  $t2 = 0…0 0000 1101 0000
  $t1 = 0…0 0011 1100 0000
and $t0, $t1, $t2 $t0 =
or $t0, $t1 $t2 $t0 =
nor $t0, $t1, $t2 $t0 =
xor $t0, $t1, $t2 $t0 =
0…0 0000 1100 0000
0…0 0011 1101 0000
1…1 1100 0010 1111
0…0 0011 0001 0000
Notes: For lecture

## Slide 33: Uses of Logical Operations
and can apply a bit pattern to a set of bits to force zeros where there is a 0 in the bit pattern. The bit pattern is called a mask, since it “conceals” the bits it is zeroing out.
Nor is often used to invert the bits of a single operand nor $t1, $t1, $zero
Along with sll and slr, and and and or are used to insert and extract sub-fields within a 32-bit word
The full instruction set also include xor

## Slide 34: MIPS Logical Instructions (Bit-Wise)
C operator | R-format | I-format
& (and) | and | andi
¦ (inclusive or) | or | ori
^ (exclusive or) | xor | xori
(none) | nor (~(a¦b)) | ---
~ (complement) | not (*) | ---
<< | sll | ---
>> (unsigned int) | srl | ---
>> (signed int)(**) | sra | ---
(*) pseudoinstruction – not rd, rs translates to nor rd, rs, $0
(**) >> is implementation-defined when the left operand is negative.
Notes: Java: << Sll and also in c
Java: >>> Srl but >> in c
Sllv: shift left logical variable : sllv $rd, $rt, $rs – do left shift of $rt indicted by the amount in the $rs field sand store in $rd
Similarly, srlv and srav instructions

## Slide 35: Coding Practice #1
Give the shortest sequence of MIPS instructions that can extract the bits in $s3 - from bit position 5 to bit position 22 - and place them in register $t0
31 23 22 5 4 0
$s3
0 . . . 0
$t0
Notes: For class handout

## Slide 36: Coding Practice #1
Give the shortest sequence of MIPS instructions that can extract the bits in $s3 - from bit position 5 to bit position 22 - and place them in register $t0
31 23 22 5 4 0
$s3
0 . . . 0
$t0
Snip: sll $t0, $s3, 9 srl $t0, $t0, 14
Notes: For lecture
Question 2.6 (from edition 3) – can do in two instructions
First instinct is to try to mask out all of the bits except bits 5 through 22 in $s3 and then do a shift right logical. But the masking can’t be done with andi.
Could do a right shift first, then a left (to clear out all of the not wanted bits), but will then need to do a last right shift to be the bits in the low order end of $t0

## Slide 37: Review: MIPS Instructions, so far
Category | Instr | OpC | Example | Meaning
Arith metic (R & I format) | add | 0 & 20 | add $s1, $s2, $s3 | $s1 = $s2 + $s3
 | subtract | 0 & 22 | sub $s1, $s2, $s3 | $s1 = $s2 - $s3
 | add immediate | 08 | addi $s1, $s2, 4 | $s1 = $s2 + 4
 | shift left logical | 0 & 00 | sll $s1, $s2, 4 | $s1 = $s2 << 4 (fill with 0’s)
 | shift right logical | 0 & 02 | srl $s1, $s2, 4 | $s1 = $s2 >> 4 (fill with 0’s)
 | shift right arithmetic | 0 & 03 | sra $s1, $s2, 4 | $s1 = $s2 >> 4 (fill with sign bit)
 | and | 0 & 24 | and $s1, $s2, $s3 | $s1 = $s2 & $s3
 | or | 0 & 25 | or $s1, $s2, $s3 | $s1 = $s2 ¦ $s3
 | nor | 0 & 27 | nor $s1, $s2, $s3 | $s1 = not ($s2 ¦ $s3)
 | and immediate | 0C | and $s1, $s2, FF00 | $s1 = $s2 & 0xFF00
 | or immediate | 0D | or $s1, $s2, FF00 | $s1 = $s2 ¦ 0xFF00
Data transfer (I format) | load word | 23 | lw $s1, 100($s2) | $s1 = Memory($s2+100)
 | store word | 2B | sw $s1, 100($s2) | Memory($s2+100) = $s1
Notes: Op code give in hex

## Slide 38: MIPS Data Types
Bit: 0, 1
Bit String: sequence of bits of a particular length
8 bits is a byte
16 bits is a half-word
32 bits is a word
64 bits is a double-word
Character:
ASCII 7 bit code
Decimal:
digits 0-9 encoded as 00002 thru 10012
two decimal digits packed per 8 bit byte
Integers: 2's complement
Floating Point

## Slide 39: Byte Addresses
Since bytes (8 bits) are so useful, most ISAs support addressing individual bytes in memory
Therefore, the memory address of a word must be a multiple of 4 (alignment restriction)
Big Endian: leftmost byte is word address
    IBM 360/370, Motorola 68k, MIPS, Sparc, HP PA
Little Endian: rightmost byte is word address
    Intel 80x86, DEC Vax, DEC Alpha (Windows NT)

## Slide 40: Addressing Objects: Endianess and Alignment
Big Endian: leftmost byte is word address
Little Endian: rightmost byte is word address
msb
lsb
little endian
big endian
Alignment restriction: requires that objects fall on address that is multiple of their size
0 1 2 3
Aligned
Not
Aligned
Notes: For class handout

## Slide 41: Addressing Objects: Endianess and Alignment
Big Endian: leftmost byte is word address
Little Endian: rightmost byte is word address
msb
lsb
3 2 1 0
little endian byte 0
0 1 2 3
big endian byte 0
Alignment restriction: requires that objects fall on address that is multiple of their size
0 1 2 3
Aligned
Not
Aligned
0 1 2 3
Notes: Class lecture
Go back and see why the number of word locations in memory is 2**30
What are the two least significant bits of a word address (always both 0)?

## Slide 42: Loading and Storing Bytes
MIPS provides special instructions to move bytes
lb $t0, 1($s3) #load byte from memory
sb $t0, 6($s3) #store byte to memory
0x28 19 8 16 bit offset
What 8 bits get loaded and stored?
  load byte places the byte from memory in the rightmost 8 bits of the destination register
    what happens to the other bits in the register?
  store byte takes the byte from the rightmost 8 bits of a register and writes it to a byte in memory
    what happens to the other bits in the memory word?
sb
0x24 19 8 16 bit offset
lbu
Notes: load byte takes the contents of the byte at the memory address specified, zero-extends it, and loads it into the register – so its really a lbu (load byte unsigned !)
Store byte leaves the other bits in the memory word intact.

## Slide 43: Example of Loading and Storing Bytes
Given following code sequence and memory state what is the state of the memory after executing the code?
add $s3, $zero, $zero
lbu $t0, 1($s3)
sb $t0, 6($s3)
Memory
0x 0 0 9 0 1 2 A 0
Data
Word
Address (Decimal)
0
4
8
12
16
20
24
0x F F F F F F F F
0x 0 1 0 0 0 4 0 2
0x 1 0 0 0 0 0 1 0
0x 0 0 0 0 0 0 0 0
0x 0 0 0 0 0 0 0 0
0x 0 0 0 0 0 0 0 0
What value is left in $t0?
What if the machine was little Endian?
What word is changed in Memory and to what?
Notes: For class handout

## Slide 44: Example of Loading and Storing Bytes
Given following code sequence and memory state what is the state of the memory after executing the code?
add $s3, $zero, $zero
lbu $t0, 1($s3)
sb $t0, 6($s3)
Memory
0x 0 0 9 0 1 2 A 0
Data
Word
Address (Decimal)
0
4
8
12
16
20
24
0x F F F F F F F F
0x 0 1 0 0 0 4 0 2
0x 1 0 0 0 0 0 1 0
0x 0 0 0 0 0 0 0 0
0x 0 0 0 0 0 0 0 0
0x 0 0 0 0 0 0 0 0
$t0 = 0x00000090
mem(4) = 0xFFFF90FF
mem(4) = 0xFF12FFFF
What value is left in $t0?
What if the machine was little Endian?
What word is changed in Memory and to what?
$t0 = 0x00000012
Notes: For lecture
Big Endian Little Endian
0 1 2 3 3 2 1 0
$t0 gets 90 $t0 gets 12
word 4 gets FFFF90FF word 4 gets FF12FFFF

## Slide 45: Loading and Storing Half Words
So MIPS also provides special instructions for half words
lh $t0, 1($s3) #load half word from memory
sh $t0, 6($s3) #store half word to memory
0x25 19 8 16 bit number
What 16 bits get loaded and stored?
  load half word places the half word from memory in the rightmost 16 bits of the destination register
    what happens to the other bits in the register?
  store half word takes the half word from the rightmost 16 bits of the register and writes it to the half word in memory
    leaving the other half word in the memory word unchanged
sh
lhu
0x29 19 8 16 bit number
Notes:   load byte takes the contents of the byte at the memory address specified, zero-extends it, and loads it into the register
  What constitutes a “legal” half word – clearly bytes 0&1 and bytes 2&3, but how about 1&2 (i.e., the two bytes from the middle of the word)?

## Slide 46: Half Word: Endianess
Big Endian: leftmost byte is word address
Little Endian: rightmost byte is word address
msb
lsb
3 2 1 0
little endian byte 0
0 1 2 3
big endian byte 0
half word 0
half word 2
Notes: What is the least significant bit of a half word address (always 0)?

## Slide 47: Review: MIPS Immediate Instructions
addi $sp, $sp, 4 #$sp = $sp + 4
slti $t0, $s2, 15 #$t0 = 1 if $s2<15
Machine format (I format):
0x0A 18 8 0x000F
Small constants are used often in typical code
  In gcc, 52% of the arithmetic operations involve constants
In MIPS immediate instructions, the constant is kept inside the instruction itself (making the common case fast !)
  Immediate format – which allows only 16 bits to be used to represent the signed (two’s complement) constant – limits values to the range +215–1 to -215
Notes: in gcc 52% of arithmetic operations involve constants – in spice its 69%
have the students answer why not – speed and limited number of registers
much faster than if loaded from memory
addi and slti do sign extend of immediate operand into the leftmost bits of the destination register (ie., copies the leftmost bit of the 16-bit immediate value into the upper 16 bits)
by contrast, ori and andi loads zero’s into the upper 16 bits and so is usually used (instead of the addi) to build 32 bit constants

## Slide 48: How About Larger Constants?
We'd also like to be able to load a 32-bit constant into a register
Must use two instructions, new "load upper immediate" instruction lui $t0, 0xAAAA
Then must get the lower order bits right, i.e., ori $t0, $t0, 0xAAAA
0x0f 0 8 1010101010101010
1010101010101010
0000000000000000
1010101010101010
0000000000000000
lui
Notes: For class handout

## Slide 49: How About Larger Constants?
We'd also like to be able to load a 32-bit constant into a register
Must use two instructions, new "load upper immediate" instruction lui $t0, 0xAAAA
Then must get the lower order bits right, i.e., ori $t0, $t0, 0xAAAA
1010101010101010
0000000000000000
1010101010101010
0000000000000000
1010101010101010 1010101010101010
0x0f 0 8 1010101010101010
lui
Psuedo instruction: --- li $t0, 0xAAAAAAAA
Notes: For lecture
sets the upper 16 bits of a constant in a register, allowing the next instruction to specify the lower 16 bits of the constant
note that lui fills the lower 16 bits of the register with zero’s
why can’t addi be used as the second instruction for this 32 bit constant?
also note – the assembler lets me specify constants larger than 16 bits in one instruction and then expands the code into two instructions (lui and ori) automatically

## Slide 50: MIPS Control Flow Instructions
MIPS conditional branch instructions:
bne $s0, $s1, Lbl #go to Lbl if $s0$s1 beq $s0, $s1, Lbl #go to Lbl if $s0=$s1
  Ex: if (i==j) h = i + j;
bne $s0, $s1, Lbl1 add $s3, $s0, $s1 Lbl1: ...
Instruction Format (I format):
0x05 16 17 ???
How is the branch destination address specified?
op rs rt 16-bit value