## Slide 1: CSE 424 Computer Architecture MIPS ISA (contd.)
Adwait Jog (http://adwaitjog.github.io/)
Based on the slides from Mary. J. Irwin (Penn State)
[Adapted from Computer Organization and Design,
5th Edition, Patterson & Hennessy,
Morgan Kaufmann]

## Slide 2: MIPS Control Flow Instructions
MIPS conditional branch instructions:
bne $s0, $s1, Lbl #go to Lbl if $s0$s1 beq $s0, $s1, Lbl #go to Lbl if $s0=$s1
  Ex: if (i==j) h = i + j;
bne $s0, $s1, Lbl1 add $s3, $s0, $s1 Lbl1: ...
Instruction Format (I format):
0x05 16 17 ???
How is the branch destination address specified?
op rs rt 16-bit value

## Slide 3: Specifying Branch Destinations
Could use a “base” register and add to it the 16-bit offset
  which register?
    Instruction Address Register (PC = program counter) - its use is automatically implied by branch
    PC gets updated (PC+4) during the Fetch cycle so that it holds the address of the next instruction
  limits the branch distance to -215 to +215-1 instructions from the (instruction after the) branch
    but most branches are local anyway
bne $s0,$s1,Lbl1
add $s3,$s0,$s1
...
Lbl1:
Could specify the memory address of the branch target - but that would require a 32-bit field
PC 
Notes: Note that two low order 0’s are concatenated to the 16 bit field giving an eighteen bit address
0111111111111111 00 = 2**15 –1 words (2**17 – 1 bytes)

## Slide 4: Disassembling Branch Destinations
The contents of the updated PC (PC+4) is added to the 16 bit branch offset which is converted into a 32-bit value by
  concatenating two low-order zeros to make it a word address and then sign-extending those 18 bits
The result is written into the PC if the branch condition is true as part of the Exec cycle - before the next Fetch cycle
PC
Add
32
32
32
32
32
offset
16
32
00
sign-extend
from the low order 16 bits of the branch instruction
branch target
address
?
Add
4
32
Fetch
PC = PC+4
Decode
Exec

## Slide 5: Offset Tradeoffs
Why not just store the word offset in the low order 16 bits? Then the two low order zeros wouldn’t have to be concatenated, it would be less confusing, …
That would limit the branch distance to -213 to +213-1 instructions from the (instruction after the) branch
And concatenating the two zero bits costs us very little in additional hardware and has no impact on the clock cycle time

## Slide 6: Assembling Branches Example
Assembly code
bne $s0, $s1, Lbl1 add $s3, $s0, $s1 Lbl1: ...
Machine Format of bne:
op rs rt 16-bit offset
I format
0x05 16 17
Remember
  After the bne instruction is fetched, the PC is updated so that it is addressing the add instruction
  The offset (plus 2 low-order zeros) is sign-extended and added to the (updated) PC
Notes: For class handout

## Slide 7: Assembling Branches Example
Assembly code
bne $s0, $s1, Lbl1 add $s3, $s0, $s1 Lbl1: ...
Machine Format of bne:
op rs rt 16-bit offset
I format
0x05 16 17
Remember
  After the bne instruction is fetched, the PC is updated so that it is addressing the add instruction
  The offset (plus 2 low-order zeros) is sign-extended and added to the (updated) PC
0x0001
Notes: For lecture.
For the code shown, the offset field should be 1 instruction (resulting in 4 = 1|00) not two instructions (resulting in 8 = 10|00) since the PC is now pointing to the add instruction (after the bne is fetched).

## Slide 8: In Support of Branch Instructions
We have beq, bne, but what about other kinds of branches (e.g., branch-if-less-than)? For this, we need yet another instruction, slt
Set on less than instruction:
slt $t0, $s0, $s1 # if $s0 < $s1 then # $t0 = 1 else # $t0 = 0
Instruction format (R format):
Alternate versions of slt
slti $t0, $s0, 25 # if $s0 < 25 then $t0=1 ...
sltu $t0, $s0, $s1 # if $s0 < $s1 then $t0=1 ...
sltiu $t0, $s0, 25 # if $s0 < 25 then $t0=1 ...
0x00 16 17 8 0x24
Notes: Unsigned (u) versus signed integer comparison

## Slide 9: More Branch Instructions
Can use slt, beq, bne, and the fixed value of 0 in register $zero to create other conditions
  less than blt $s1, $s2, Label
  less than or equal to ble $s1, $s2, Label
  greater than bgt $s1, $s2, Label
  great than or equal to bge $s1, $s2, Label
Such branches are included in the instruction set as pseudo instructions - recognized (and expanded) by the assembler
  Its why the assembler needs a reserved register ($at)
Notes: For class handout

## Slide 10: More Branch Instructions
Can use slt, beq, bne, and the fixed value of 0 in register $zero to create other conditions
  less than blt $s1, $s2, Label
  less than or equal to ble $s1, $s2, Label
  greater than bgt $s1, $s2, Label
  great than or equal to bge $s1, $s2, Label
slt $at, $s1, $s2 #$at set to 1 if
bne $at, $zero, Label #$s1 < $s2
Such branches are included in the instruction set as pseudo instructions - recognized (and expanded) by the assembler
  Its why the assembler needs a reserved register ($at)
Notes: For lecture
blt $s1,$s2 Label =
slt $at,$s1,$s2 #at gets 1 if $s1 < $s2
bne $at,$zero,Label

## Slide 11: Another Instruction for Changing Flow
MIPS also has an unconditional branch instruction or jump instruction: j Lbl #go to Lbl
Example: if (i!=j) h=i+j; else h=i-j;
beq $s0, $s1, Else add $s3, $s0, $s1 j Exit Else: sub $s3, $s0, $s1 Exit: ...
Notes: If-then-else code compilation

## Slide 12: Assembling Jumps
Instruction:
j Lbl #go to Lbl
Machine Format (J format):
op 26-bit address
0x02 ????
How is the jump destination address specified?
  As an absolute address formed by
    concatenating 00 as the 2 low-order bits to make it a word address
    concatenating the upper 4 bits of the current PC (now PC+4)

## Slide 13: Disassembling Jump Destinations
The low-order 26 bits of the jump instruction is converted into a 32-bit jump destination address by
  concatenating two low-order zeros to create an 28 bit (word) address and then concatenating the upper 4 bits of the current PC (now PC+4) to create a 32 bit (word) address
that is put into the PC prior to the next Fetch cycle
PC
4
32
26
32
00
from the low order 26 bits of the jump instruction
Fetch
PC = PC+4
Decode
Exec
Notes: The loader and linker must be careful to avoid placing a program across an address boundary of 256 MB (64 million instructions) – otherwise a jump must be replaced by a jump register instruction preceded by other instructions to load the full 32-bit address into a register

## Slide 14: Review: MIPS R3000 ISA
Instruction Categories
  Load/Store
  Computational
  Jump and Branch
  Floating Point
    coprocessor
  Memory Management
  Special
3 Instruction Formats: all 32 bits wide
R0 - R31
PC
HI
LO
OP
rs
rt
rd
shamt
funct
OP
rs
rt
16 bit number
OP
26 bit jump target
Registers
R format
I format
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
J format

## Slide 15: Review: Addressing Modes, so far
1. Register addressing
op rs rt rd funct
Register
word operand
3. Immediate addressing
op rs rt operand
op rs rt offset
2. Base (displacement) addressing
base register
Memory
word or byte operand
4. Pseudo-direct addressing
op jump address
Program Counter (PC)
Memory
jump destination instruction
||

## Slide 16: Branching Far Away
What if the branch destination is further away than can be captured in 16 bits?
The assembler comes to the rescue – it inserts an unconditional jump to the branch target and inverts the condition
beq $s0, $s1, L1
becomes
bne $s0, $s1, L2
j L1
L2:

## Slide 17: Assembling Branches and Jumps
Assemble the MIPS machine code for the following code sequence. Assume that the addr of the beq instr is 0x00400020hex
beq $s0, $s1, Else add $s3, $s0, $s1 j Exit Else: sub $s3, $s0, $s1 Exit: ...
Notes: For class handout

## Slide 18: Assembling Branches and Jumps
Assemble the MIPS machine code for the following code sequence. Assume that the addr of the beq instr is 0x00400020hex
beq $s0, $s1, Else add $s3, $s0, $s1 j Exit Else: sub $s3, $s0, $s1 Exit: ...
0x00400020 4 16 17 2
0x00400024 0 16 17 19 0 0x20
0x00400028 2 0000 0100 0 ... 0 0011 002
0x0040002c 0 16 17 19 0 0x22
0x00400030 ...
jmp dst = (0x0) 0x040003 002(002)
= 0x00400030
Notes: For lecture
0x00400020 4 16 17 2
0x00400024 0 16 17 19 0 32
0x00400028 2 0000 0100 0000 0000 0000 0011 00 = (0) 0x040003 00(00)
0x0040002c 0 16 17 19 0 34
0x00400030 . . .
Note: for the jump address the decimal number is 32+8 +8 = 48; which is 3 in Hex notation. So, the address is 0x00400030.

## Slide 19: Compiling While Loops
Compile the assembly code for the C while loop where i is in $s0, j is in $s1, and k is in $s2
while (i!=k) i=i+j;
Basic block – A sequence of instructions without branches (except at the end) and without branch targets (except at the beginning)
Notes: For class handout

## Slide 20: Compiling While Loops
Compile the assembly code for the C while loop where i is in $s0, j is in $s1, and k is in $s2
while (i!=k) i=i+j;
Loop: beq $s0, $s2, Exit add $s0, $s0, $s1 j Loop Exit: . . .
Basic block – A sequence of instructions without branches (except at the end) and without branch targets (except at the beginning)
Notes: For lecture
Loop beq $s0, $s2, Exit
add $s0, $s0, $s1
j Loop
Exit: . . .

## Slide 21: Review: MIPS Instructions, so far
Category | Instr | OpC | Example | Meaning
Arithmetic (R & I format) | add | 0 & 20 | add $s1, $s2, $s3 | $s1 = $s2 + $s3
 | subtract | 0 & 22 | sub $s1, $s2, $s3 | $s1 = $s2 - $s3
 | add immediate | 08 | addi $s1, $s2, 4 | $s1 = $s2 + 4
 | shift left logical | 0 & 00 | sll $s1, $s2, 4 | $s1 = $s2 << 4
 | shift right logical | 0 & 02 | srl $s1, $s2, 4 | $s1 = $s2 >> 4 (fill with zeros)
 | shift right arithmetic | 0 & 03 | sra $s1, $s2, 4 | $s1 = $s2 >> 4 (fill with sign bit)
 | and | 0 & 24 | and $s1, $s2, $s3 | $s1 = $s2 & $s3
 | or | 0 & 25 | or $s1, $s2, $s3 | $s1 = $s2 ¦ $s3
 | nor | 0 & 27 | nor $s1, $s2, $s3 | $s1 = not ($s2 ¦ $s3)
 | and immediate | 0C | and $s1, $s2, FF00 | $s1 = $s2 & 0xFF00
 | or immediate | 0D | or $s1, $s2, FF00 | $s1 = $s2 ¦ 0xFF00
 | load upper immediate | 0F | lui $s1, 0xFFFF | $s1 = 0xFFFF0000

## Slide 22: Review: MIPS Instructions, so far
Category | Instr | OpC | Example | Meaning
Data transfer (I format) | load word | 23 | lw $s1, 100($s2) | $s1 = Memory($s2+100)
 | store word | 2B | sw $s1, 100($s2) | Memory($s2+100) = $s1
 | load byte | 24 | lbu $s1, 101($s2) | $s1 = Memory($s2+101)
 | store byte | 28 | sb $s1, 101($s2) | Memory($s2+101) = $s1
 | load half | 25 | lhu $s1, 101($s2) | $s1 = Memory($s2+102)
 | store half | 29 | sh $s1, 101($s2) | Memory($s2+102) = $s1
Cond. branch (I & R format) | br on equal | 04 | beq $s1, $s2, L | if ($s1==$s2) go to L
 | br on not equal | 05 | bne $s1, $s2, L | if ($s1 !=$s2) go to L
 | set on less than immediate | 0A | slti $s1, $s2, 100 | if ($s2<100) $s1=1; else $s1=0
 | set on less than | 0 & 2A | slt $s1, $s2, $s3 | if ($s2<$s3) $s1=1; else $s1=0
Uncond. jump | jump | 02 | j 2500 | go to 10000
 | jump register | 0 & 08 | jr $t1 | go to $t1
 | jump and link | 03 | jal 2500 | go to 10000; $ra=PC+4

## Slide 23: Review: MIPS R3000 ISA
Instruction Categories
  Load/Store
  Computational
  Jump and Branch
  Floating Point
    coprocessor
  Memory Management
  Special
3 Instruction Formats: all 32 bits wide
R0 - R31
PC
HI
LO
OP
rs
rt
rd
shamt
funct
OP
rs
rt
16 bit number
OP
26 bit jump target
Registers
R format
I format
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
J format

## Slide 24: MIPS Operand Addressing Modes Summary
Register addressing – operand is in a register
Base (displacement) addressing – address of operand in memory is the sum of a register and a 16-bit constant contained within the instruction
Immediate addressing – operand is a 16-bit constant contained within the instruction
1. Register addressing
op rs rt rd funct
Register
word operand
op rs rt offset
2. Base addressing
base register
Memory
Word, halfword or byte operand
3. Immediate addressing
op rs rt operand
Fetch
PC = PC+4
Decode
Exec

## Slide 25: MIPS Instruction Addressing Modes Summary
PC-relative addressing – instruction’s address in memory is the sum of the PC and a 16-bit constant contained within the instruction
Pseudo-direct addressing – instruction’s address in memory is the 26-bit constant contained within the instruction concatenated with the upper 4 bits of the PC
4. PC-relative addressing
op rs rt offset
Program Counter (PC)
Memory
branch destination instruction
5. Pseudo-direct addressing
op jump address
Program Counter (PC)
Memory
jump destination instruction
||

## Slide 26: Yet Another Instruction for Changing Flow
Most higher level languages have case or switch statements allowing the code to select one of many alternatives depending on a single value
Instruction:
jr $t1 #go to address in $t1
Machine format (R format):
op rs funct
0x00 9 0 0 0 0x08

## Slide 27: Compiling a Case (Switch) Statement
  switch (k) {
  case 0: h=i+j; break; /*k=0*/
  case 1: h=i+h; break; /*k=1*/
  case 2: h=i-j; break; /*k=2*/
Assume three sequential words in memory starting at the address in $t4 have the addresses of the labels L0, L1, and L2 and k is in $s2
add $t1, $s2, $s2 #$t1 = 2*k
  add $t1, $t1, $t1 #$t1 = 4*k
  add $t1, $t1, $t4 #$t1 = addr of JumpT[k]
  lw $t0, 0($t1) #$t0 = JumpT[k]
  jr $t0 #jump based on $t0
L0: add $s3, $s0, $s1 #k=0 so h=i+j
j Exit
L1: add $s3, $s0, $s3 #k=1 so h=i+h
j Exit
L2: sub $s3, $s0, $s1 #k=2 so h=i-j
Exit: . . .
$t4
L2
L1
L0
Memory
Notes: Skips the code to check first to make sure k is in the range of 0 to 2

## Slide 28: Compiling Another While Loop
Compile the assembly code for the C while loop where i is in $s0, k is in $s1, and the base address of the array save is in $s2
while (save[i] == k) i += 1;
Notes: For class handout

## Slide 29: Compiling Another While Loop
Compile the assembly code for the C while loop where i is in $s0, k is in $s1, and the base address of the array save is in $s2
while (save[i] == k) i += 1;
Loop: sll $t1, $s0, 2 add $t1, $t1, $s2 lw $t0, 0($t1) bne $t0, $s1, Exit addi $s0, $s0, 1 j Loop Exit: . . .
Notes: For lecture

## Slide 30: Programming Styles
Procedures (subroutines, functions) allow the programmer to structure programs making them
  easier to understand and debug and
  allowing code to be reused
Procedures allow the programmer to concentrate on one portion of the code at a time
  parameters act as barriers between the procedure and the rest of the program and data, allowing the procedure to be passed values (arguments) and to return values (results)
Notes: barriers concept is important!!

## Slide 31: Six Steps in Execution of a Procedure
Main routine (caller) places parameters in a place where the procedure (callee) can access them
  $a0 - $a3: four argument registers
Caller transfers control to the callee
Callee acquires the storage resources needed
Callee performs the desired task
Callee places the result value in a place where the caller can access it
  $v0 - $v1: two value registers for result values
Callee returns control to the caller
  $ra: one return address register to return to the point of origin

## Slide 32: Review: MIPS Register Naming Convention
Nick Name | Register Number | Usage | Preserve on call?
$zero | 0 | constant 0 (hardware) | n.a.
$at | 1 | reserved for assembler | n.a.
$v0 - $v1 | 2-3 | returned values | no
$a0 - $a3 | 4-7 | arguments | no
$t0 - $t7 | 8-15 | temporaries | no
$s0 - $s7 | 16-23 | saved values | yes
$t8 - $t9 | 24-25 | temporaries | no
$k0 - $k1 | 26-27 | reserved for OS | n.a.
$gp | 28 | global pointer | yes
$sp | 29 | stack pointer | yes
$fp | 30 | frame pointer | yes
$ra | 31 | return addr (hardware) | yes

## Slide 33: Instruction for Calling a Procedure
MIPS procedure call instruction: jal ProcAddress #jump and link
Saves PC+4 in register $ra as the link to the following instruction to set up the procedure return and then performs the jump operation
Machine format (J format):
Then can do procedure return with just
jr $ra #return
op 26 bit address
0x03 ????
Notes: jr jumps to the address stored in the register – in this case $ra – which is just what we want.

## Slide 34: Basic Procedure Flow
For a procedure that computes the GCD of two values i (in $t0) and j (in $t1)
gcd(i,j);
The caller puts the i and j (the parameters values) in $a0 and $a1 and issues a
jal gcd #jump to routine gcd
The callee computes the GCD, puts the result in $v0, and returns control to the caller using
gcd: . . . #code to compute gcd
jr $ra #return

## Slide 35: Spilling Registers
What if the callee needs to use more registers than allocated to argument and return values?
  callee uses a stack – a last-in-first-out queue
low addr
high addr
$sp
One of the general registers, $sp ($29), is used to address the stack (which “grows” from high address to low address)
  add data onto the stack – push
    $sp = $sp – 4 data on stack at new $sp
  remove data from the stack – pop
    data from stack at $sp $sp = $sp + 4
top of stack
Notes: Note that temporary registers $t0 through $t9 can also be used as by MIPS convention they are not preserved by the callee (kept intact) across subroutine boundaries
However, saved registers $s0 through $s7 must be preserved by the calle - I.e., if the callee uses one, it must first save it and then restore it to its old value before returning control to the caller

## Slide 36: Allocating Space on the Stack
The segment of the stack containing a procedure’s saved registers and local variables is its procedure frame (aka activation record)
  The frame pointer ($fp) points to the first word of the frame of a procedure – providing a stable “base” register for the procedure
  $fp is initialized using $sp on a call and $sp is restored using $fp on a return
low addr
high addr
$sp
Saved argument regs (if any)
Saved return addr
Saved local regs (if any)
Local arrays & structures (if any)
$fp
Notes: On the other hand, the stack pointer (sp) might change during the procedure (not the case for all of our examples) so references to a local variable in memory might have different offsets wrt the sp depending on where they are in the procedure.

## Slide 37: Allocating Space in the Memory
There is also a static data segment area for storing constants and other static variables (e.g., arrays)
And a dynamic data segment (aka heap) area for structures that grow and shrink (e.g., linked lists)
  Allocate space on the heap with malloc() and free it with free()in C
Memory
0x 0000 0000
Text
(Your code)
Reserved
Static data
0x 0040 0000
0x 1000 0000
0x 1000 8000
0x 7FFFFFFC
Stack
Dynamic data
(heap)
$fp
$gp
PC
$sp
Notes: Stack and heap grow towards each other.
Malloc() allocates space on the heap and returns a pointer to it. Memory allocation is controlled by programs (in C) and is the source of many common and difficult bugs. Forgetting to free space leads to “memory leak” and the need for “garbage collection” and freeing space to early to “dangling pointers”.

## Slide 38: Compiling a C Leaf Procedure
Leaf procedures are ones that do not call other procedures. Give the MIPS assembler code for
int leaf_ex (int g, int h, int i, int j)
{ int f;
f = (g+h) – (i+j);
return f; }
where g, h, i, and j are in $a0, $a1, $a2, $a3
Notes: For class handout

## Slide 39: Compiling a C Leaf Procedure
Leaf procedures are ones that do not call other procedures. Give the MIPS assembler code for
int leaf_ex (int g, int h, int i, int j)
{ int f;
f = (g+h) – (i+j);
return f; }
where g, h, i, and j are in $a0, $a1, $a2, $a3
leaf_ex: addi $sp,$sp,-8 #make stack room
sw $t1,4($sp) #save $t1 on stack
sw $t0,0($sp) #save $t0 on stack
add $t0,$a0,$a1
add $t1,$a2,$a3
sub $v0,$t0,$t1
lw $t0,0($sp) #restore $t0
lw $t1,4($sp) #restore $t1
addi $sp,$sp,8 #adjust stack ptr
jr $ra
Notes: For lecture
When using temporary registers, must assume their old values must be saved and restored.
(But the convention is to not expect them to be saved, so don’t really have to go through the stack pushing and popping.)
Show the stack contents on the board as you progress through the code

## Slide 40: Stack Usage
Pushing arguments on the stack
leaf_ex: addi $sp,$sp,-8
sw $t1,4($sp)
sw $t0,0($sp)
high addr
$sp
old top of stack
$sp-8
0(updated $sp)
4(updated $sp)
new top of stack
Popping arguments from the stack
lw $t0,0($sp)
lw $t1,4($sp)
addi $sp,$sp,8
high addr
$sp+8
new top of stack
$sp
0(original $sp)
4(original $sp)
old top of stack

## Slide 41: Compiling a Recursive Procedure
Calculating factorial:
int fact (int n)
{
if (n < 1) return 1;
else return (n * fact (n-1));
}
Recursive procedure (one that calls itself!)
  fact (0) = 1
  fact (1) = 1 * 1 = 1
  fact (2) = 2 * 1 * 1 = 2
  fact (3) = 3 * 2 * 1 * 1 = 6
  fact (4) = 4 * 3 * 2 * 1 * 1 = 24
  . . .
Assume n is passed in $a0; result returned in $v0

## Slide 42: Compiling a Recursive Procedure
fact: addi $sp, $sp, -8 #adjust stack pointer
sw $ra, 4($sp) #save return address
sw $a0, 0($sp) #save argument n
slt $t0, $a0, 1 #test for n < 1
beq $t0, $zero, L1 #if n >=1, go to L1
addi $v0, $zero, 1 #else return 1 in $v0
addi $sp, $sp, 8 #adjust stack pointer
jr $ra #return to caller
L1: addi $a0, $a0, -1 #n >=1, so decrement n
jal fact #call fact with (n-1)
#this is where fact returns
bk_f: lw $a0, 0($sp) #restore argument n
lw $ra, 4($sp) #restore return address
addi $sp, $sp, 8 #adjust stack pointer
mul $v0, $a0, $v0 #$v0 = n * fact(n-1)
jr $ra #return to caller
int fact (int n)
{
if (n < 1)
return 1;
else
return (n * fact (n-1));
}
Notes: Note, no need to load $ra, and $a0, since they have not changed values (expect when n is >= to 1 as on next page)

## Slide 43: A Look at the Stack for $a0 = 2
1
caller rt addr
caller rt addr
 $sp
$ra
$a0
$v0
$a0 = 2
2
bk_f
old TOS
int fact (int n)
{
if (n < 1)
return 1;
else
return (n * fact (n-1));
}
fact: addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
slt $t0, $a0, 1
beq $t0, $zero, L1
addi $v0, $zero, 1
addi $sp, $sp, 8
jr $ra
L1: addi $a0, $a0, -1
jal fact
bk_f: lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
mul $v0, $a0, $v0
jr $ra
Notes: For lecture
NEXT TIME - Add tracking of the PC to the animation!!

## Slide 44: A Look at the Stack for $a0 = 2
1
caller rt addr
 $sp
$ra
$a0
$v0
$a0 = 2
bk_f
old TOS
Stack state after execution of first encounter with the jal instruction (second call to fact routine with $a0 now holding 1)
  saved return address to caller routine (i.e., location in the main routine where first call to fact is made) on the stack
  saved original value of $a0 on the stack
int fact (int n)
{
if (n < 1)
return 1;
else
return (n * fact (n-1));
}
Notes: For lecture
NEXT TIME - Add tracking of the PC to the animation!!

## Slide 45: A Look at the Stack for $a0 = 2
1
bk_f
 $sp
$ra
$a0
$v0
$a0 = 1
0
bk_f
old TOS
int fact (int n)
{
if (n < 1)
return 1;
else
return (n * fact (n-1));
}
caller rt addr
$a0 = 2
fact: addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
slt $t0, $a0, 1
beq $t0, $zero, L1
addi $v0, $zero, 1
addi $sp, $sp, 8
jr $ra
L1: addi $a0, $a0, -1
jal fact
bk_f: lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
mul $v0, $a0, $v0
jr $ra
Notes: For lecture
NEXT TIME - Add tracking of the PC to the animation!!

## Slide 46: A Look at the Stack for $a0 = 2
caller rt addr
$ra
$a0
$v0
$a0 = 2
0
bk_f
old TOS
 $sp
$a0 = 1
bk_f
bk_f
Stack state after execution of second encounter with the jal instruction (third call to fact routine with $a0 now holding 0)
  saved return address of instruction in caller routine (instruction after jal) on the stack
  saved previous value of $a0 on the stack
int fact (int n)
{
if (n < 1)
return 1;
else
return (n * fact (n-1));
}
Notes: For lecture

## Slide 47: A Look at the Stack for $a0 = 2
1
bk_f
 $sp
$ra
$a0
$v0
$a0 = 1
0
bk_f
old TOS
int fact (int n)
{
if (n < 1)
return 1;
else
return (n * fact (n-1));
}
caller rt addr
$a0 = 2
fact: addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
slt $t0, $a0, 1
beq $t0, $zero, L1
addi $v0, $zero, 1
addi $sp, $sp, 8
jr $ra
L1: addi $a0, $a0, -1
jal fact
bk_f: lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
mul $v0, $a0, $v0
jr $ra
bk_f
$a0 = 0
Notes: For lecture
NEXT TIME - Add tracking of the PC to the animation!!

## Slide 48: A Look at the Stack for $a0 = 2
1
bk_f
 $sp
$ra
$a0
$v0
$a0 = 1
0
bk_f
old TOS
int fact (int n)
{
if (n < 1)
return 1;
else
return (n * fact (n-1));
}
caller rt addr
$a0 = 2
Stack state after execution of first encounter with the first jr instruction ($v0 initialized to 1)
  stack pointer updated to point to third call to fact
Notes: For lecture
NEXT TIME - Add tracking of the PC to the animation!!

## Slide 49: A Look at the Stack for $a0 = 2
1
 $sp
$ra
$a0
$v0
0
bk_f
old TOS
int fact (int n)
{
if (n < 1)
return 1;
else
return (n * fact (n-1));
}
caller rt addr
$a0 = 2
fact: addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
slt $t0, $a0, 1
beq $t0, $zero, L1
addi $v0, $zero, 1
addi $sp, $sp, 8
jr $ra
L1: addi $a0, $a0, -1
jal fact
bk_f: lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
mul $v0, $a0, $v0
jr $ra
bk_f
$a0 = 1
1
1*1 = 1
Notes: For lecture
NEXT TIME - Add tracking of the PC to the animation!!

## Slide 50: A Look at the Stack for $a0 = 2
 $sp
$ra
$a0
$v0
bk_f
old TOS
int fact (int n)
{
if (n < 1)
return 1;
else
return (n * fact (n-1));
}
caller rt addr
$a0 = 2
1
1
Stack state after execution of first encounter with the second jr instruction (return from fact routine after updating $v0 to 1 * 1)
  return address to caller routine (bk_f in fact routine) restored to $ra from the stack
  previous value of $a0 restored from the stack
  stack pointer updated to point to second call to fact
Notes: For lecture
NEXT TIME - Add tracking of the PC to the animation!!

## Slide 51: A Look at the Stack for $a0 = 2
1
 $sp
$ra
$a0
$v0
1
bk_f
old TOS
int fact (int n)
{
if (n < 1)
return 1;
else
return (n * fact (n-1));
}
caller rt addr
$a0 = 2
fact: addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
slt $t0, $a0, 1
beq $t0, $zero, L1
addi $v0, $zero, 1
addi $sp, $sp, 8
jr $ra
L1: addi $a0, $a0, -1
jal fact
bk_f: lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
mul $v0, $a0, $v0
jr $ra
2
2*1 = 2
caller rt addr
Notes: For lecture
NEXT TIME - Add tracking of the PC to the animation!!

## Slide 52: A Look at the Stack for $a0 = 2
 $sp
$ra
$a0
$v0
old TOS
2
2
caller rt addr
Stack state after execution of second encounter with the second jr instruction (return from fact routine after updating $v0 to 1 * 1 * 2)
  return address to caller routine (main routine) restored to $ra from the stack
  original value of $a0 restored from the stack
  stack pointer updated to point to first call to fact
int fact (int n)
{
if (n < 1)
return 1;
else
return (n * fact (n-1));
}
Notes: For lecture

## Slide 53: String Copy in C (Read on your own)
Copy string y to string x (null byte termination)
void stcp (char x[], char y[])
{ int i;
i = 0;
while ((x[i] = y[i]) != ‘\0’)
i += 1; }
Assume the base addresses for arrays x and y are found in $a0 and $a1, and i is in $s0

## Slide 54: String Copy (Read on your own)
stcp: addi $sp, $sp, -4 #adjust stack pointer
sw $s0, 0($sp) #save $s0 on stack
add $s0, $zero, $zero #i = 0 + 0
#loop in L1 until encounter NULL
L1: add $t1, $s0, $a1 #address of y[i] in $t1
lbu $t2, 0($t1) #$t2 = y[i]
add $t3, $s0, $a0 #address of x[i] in $t1
sb $t2, 0($t3) #x[i] = y[i]
beq $t2, $zero, L2 #if y[i] ==0, done
addi $s0, $s0, 1 #i = i + 1
j L1 #go to copy more chars
#almost done, just pop the stack
L2: lw $s0, 0($sp) #restore $s0 from stack
addi $sp, $sp, 4 #adjust stack pointer
jr $ra #return to caller

## Slide 55: Nested Procedures (Read on your own)
What happens to return addresses with nested procedures?
int rt_1 (int i) {
if (i == 0) return 0;
else return rt_2(i-1); }
caller: jal rt_1 next: . . .
rt_1: bne $a0, $zero, to_2
add $v0, $zero, $zero
jr $ra
to_2: addi $a0, $a0, -1 #(for i-1)
jal rt_2
jr $ra
rt_2: . . .
Notes: So caller must save $ra on the stack and callee must save any other registers that it uses on the stack

## Slide 56: Nested Procedures Outcome
caller: jal rt_1 next: . . .
rt_1: bne $a0, $zero, to_2
add $v0, $zero, $zero
jr $ra
to_2: addi $a0, $a0, -1
jal rt_2
jr $ra
rt_2: . . .
On the call to rt_1, the return address (next in the caller routine) gets stored in $ra. What happens to the value in $ra (when i != 0) when rt_1 makes a call to rt_2?
Notes: So caller must save $ra on the stack and callee must save any other registers that it uses on the stack

## Slide 57: Saving the Return Address, Part 1
Nested procedures (i passed in $a0, return value in $v0)
rt_1: bne $a0, $zero, to_2
add $v0, $zero, $zero
jr $ra
to_2: addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
addi $a0, $a0, -1
jal rt_2
bk_2: lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
jr $ra
Save the return address (and arguments) on the stack
low addr
high addr
$sp
$ra
old TOS
Notes: For class handout

## Slide 58: Saving the Return Address, Part 1
Nested procedures (i passed in $a0, return value in $v0)
rt_1: bne $a0, $zero, to_2
add $v0, $zero, $zero
jr $ra
to_2: addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
addi $a0, $a0, -1
jal rt_2
bk_2: lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
jr $ra
Save the return address (and arguments) on the stack
caller rt addr
high addr
 $sp
$sp
low addr
old $a0
$ra
caller rt addr
bk_2
old TOS
$pc 
$pc 
$pc 
$pc 
$pc 
Notes: For lecture
Note that the original values of $ra and I ($a0) are restored on return

## Slide 59: Saving the Return Address, Part 2
Nested procedures (i passed in $a0, return value in $v0)
rt_1: bne $a0, $zero, to_2
add $v0, $zero, $zero
jr $ra
to_2: addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
addi $a0, $a0, -1
jal rt_2
bk_2: lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
jr $ra
Save the return address (and arguments) on the stack
low addr
high addr
$sp
$ra
old TOS
Notes: For class handout

## Slide 60: Saving the Return Address, Part 2
Nested procedures (i passed in $a0, return value in $v0)
rt_1: bne $a0, $zero, to_2
add $v0, $zero, $zero
jr $ra
to_2: addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
addi $a0, $a0, -1
jal rt_2
bk_2: lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
jr $ra
Save the return address (and arguments) on the stack
caller rt addr
high addr
$sp
 $sp
low addr
old $a0
$ra
bk_2
caller rt addr
old TOS
$pc 
$pc 
Notes: For lecture

## Slide 61: Compiling a Recursive Procedure
A recursive procedure in C for calculating the factorial
int fact (int n) {
if (n < 1) return 1;
else return (n * fact (n-1)); }
A recursive procedure (one that calls itself!)
  fact (0) = 1
  fact (1) = 1 * 1 = 1
  fact (2) = 2 * 1 * 1 = 2
  fact (3) = 3 * 2 * 1 * 1 = 6
  fact (4) = 4 * 3 * 2 * 1 * 1 = 24
  . . .
Assume n is passed in $a0; result returned in $v0

## Slide 62: Compiling a Recursive Procedure
fact: addi $sp, $sp, -8 #adjust stack pointer
sw $ra, 4($sp) #save return address
sw $a0, 0($sp) #save argument n
slti $t0, $a0, 1 #test for n < 1
beq $t0, $zero, L1 #if n >=1, go to L1
addi $v0, $zero, 1 #else return 1 in $v0
addi $sp, $sp, 8 #adjust stack pointer
jr $ra #return to caller (1st)
L1: addi $a0, $a0, -1 #n >=1, so decrement n
jal fact #call fact with (n-1)
#this is where fact returns
bk_f: lw $a0, 0($sp) #restore argument n
lw $ra, 4($sp) #restore return address
addi $sp, $sp, 8 #adjust stack pointer
mul $v0, $a0, $v0 #$v0 = n * fact(n-1)
jr $ra #return to caller (2nd)
Notes: Note, no need to load $ra, and $a0, since they have not changed values (expect when n is >= to 1 as on next page)
We assume a multiply instruction is available, even though we haven’t covered it yet!

## Slide 63: Recursive Procedure Structure
Main routine
Does input, output, sets up the parameters to pass to the recursive procedure in $a0 through $a3 and then calls the recursive procedure with a jal
Recursive procedure
From the arguments sent to it by the Main routine in $a0 and $a3, computes the result(s) of the function and puts those values in $v0 and $v1 before returning to the Main routine with a jr
Recursive procedure call themselves with a jal (typically from somewhere in the middle of the code) and return to themselves with a jr

## Slide 64: A Look at the Stack for $a0 = 2, Part 1
$sp
$ra
$a0
$v0
old TOS
Stack state after execution of the first encounter with jal (second call to fact routine after which $a0 will be holding 1)
  saved return address to caller routine (i.e., location in the main routine where first call to fact is made) on the stack
  saved original value of $a0 on the stack
Notes: For class handout

## Slide 65: A Look at the Stack for $a0 = 2, Part 1
 $sp
$ra
$a0
$v0
$sp
caller rt addr
caller rt addr
$a0 = 2
2
1
bk_f
old TOS
Stack state after execution of the first encounter with jal (second call to fact routine after which $a0 will be holding 1)
  have saved return address to caller routine (i.e., location in the main routine where first call to fact is made) on the stack
  saved original value of $a0 on the stack
Notes: For lecture
NEXT TIME - Add tracking of the PC to the animation!!

## Slide 66: A Look at the Stack for $a0 = 2, Part 2
$ra
$a0
$v0
old TOS
Stack state after execution of the second encounter with jal (third call to fact routine after which $a0 will be holding 0)
  save return address of instruction in caller routine (instruction after jal) on the stack
  save previous value of $a0 on the stack
Notes: For class handout

## Slide 67: A Look at the Stack for $a0 = 2, Part 2
$ra
$a0
$v0
 $sp
caller rt addr
$a0 = 2
1
0
bk_f
old TOS
$sp
$a0 = 1
bk_f
bk_f
Stack state after execution of the second encounter with jal (third call to fact routine after which $a0 will be holding 0)
  saved return address of instruction in caller routine (instruction after jal) on the stack
  saved previous value of $a0 on the stack
Notes: For lecture

## Slide 68: A Look at the Stack for $a0 = 2, Part 3
$ra
$a0
$v0
old TOS
Stack state after execution of the first encounter with the 1st jr
  stack pointer updated to point to third call to fact and then updated again
  $v0 initialized to 1
Notes: For class handout

## Slide 69: A Look at the Stack for $a0 = 2, Part 3
$ra
$a0
$v0
 $sp
bk_f
$a0 = 1
0
old TOS
 $sp
$a0 = 0
bk_f
bk_f
$a0 = 2
caller rt addr
1
$sp
Stack state after execution of the first encounter with the 1st jr
  stack pointer updated to point to third call to fact and then updated again
  $v0 initialized to 1
Notes: For lecture

## Slide 70: A Look at the Stack for $a0 = 2, Part 4
$ra
$a0
$v0
old TOS
Stack state after execution of the first encounter with the 2nd jr (returns from fact routine after updating $v0 to 1 * 1)
  return address to caller routine (bk_f in fact routine) restored to $ra from the stack
  previous value of $a0 restored from the stack
  fact routine computes the new $v0 (1 * 1)
  stack pointer updated to point to second call to fact
Notes: For class handout

## Slide 71: A Look at the Stack for $a0 = 2, Part 4
$ra
$a0
$v0
 $sp
bk_f
$a0 = 1
0
old TOS
$a0 = 0
bk_f
$a0 = 2
caller rt addr
1
$sp
1
bk_f
1 * 1
Stack state after execution of the first encounter with the 2nd jr (returns from fact routine after updating $v0 to 1 * 1)
  return address to caller routine (bk_f in fact routine) restored to $ra from the stack
  previous value of $a0 restored from the stack
  fact routine computes the new $v0 (1 * 1)
  stack pointer updated to point to second call to fact
Notes: For lecture

## Slide 72: A Look at the Stack for $a0 = 2, Part 5
$sp
$ra
$a0
$v0
old TOS
Stack state after execution of the second encounter with the 2nd jr (return from fact routine after updating $v0 to 2 * 1 * 1)
  return address to caller routine (main routine) restored to $ra from the stack
  original value of $a0 restored from the stack
  fact routine computes the new $v0 (2 * 1 * 1)
  stack pointer updated to point to first call to fact
Notes: For class handout

## Slide 73: A Look at the Stack for $a0 = 2, Part 5
$ra
$a0
$v0
 $sp
bk_f
$a0 = 1
1
old TOS
$a0 = 0
bk_f
$a0 = 2
caller rt addr
1 * 1
$sp
2
bk_f
2 * 1 * 1
Stack state after execution of the second encounter with the 2nd jr (return from fact routine after updating $v0 to 2 * 1 * 1)
  return address to caller routine (main routine) restored to $ra from the stack
  original value of $a0 restored from the stack
  fact routine computes the new $v0 (2 * 1 * 1)
  stack pointer updated to point to first call to fact
caller rt addr
Notes: For lecture