## Slide 1: CSE 424 Computer Architecture MIPS Datapath Components and Design
Adwait Jog (http://adwaitjog.github.io/)
Based on the slides from Mary. J. Irwin (Penn State)
[Adapted from Computer Organization and Design,
5th Edition, Patterson & Hennessy,
Morgan Kaufmann]

## Slide 2: The Processor: Datapath & Control
We're ready to look at an implementation of the MIPS simplified to contain only:
  memory-reference instructions: lw, sw
  arithmetic-logical instructions: add, addu, sub, subu, and, or, xor, nor, slt, sltu
  arithmetic-logical immediate instructions: addi, addiu, andi, ori, xori, slti, sltiu
  control flow instructions: beq, j
Generic implementation:
  use the program counter (PC) to supply the instruction address and fetch the instruction from memory (and update the PC)
  decode the instruction (and read registers)
  execute the instruction
Fetch
PC = PC+4
Decode
Exec
Notes: memory reference use ALU to compute addresses
arithmetic use the ALU to do the require arithmetic
control use the ALU to compute branch conditions.

## Slide 3: Abstract Implementation View
Two types of functional units:
  elements that operate on data values (combinational)
  elements that contain state (sequential)
Single cycle operation
Split memory (Harvard) model - one memory for instructions and one for data
Von Neumann architecture: Uses one combined memory for instruction and data
Address
Instruction
Instruction
Memory
Write Data
Reg Addr
Reg Addr
Reg Addr
Register
File
ALU
Data
Memory
Address
Write Data
Read Data
PC
Read
Data
Read
Data
Notes: Have the class tell which is which in the picture - combinational and sequential

## Slide 4: Clocking Methodologies
Clocking methodology defines when signals can be read and when they can be written
falling (negative) edge
rising (positive) edge
clock cycle
clock rate = 1/(clock cycle)
e.g., 10 nsec clock cycle = 100 MHz clock rate
1 nsec clock cycle = 1 GHz clock rate
State element design choices
  level sensitive latch
  edge-triggered (master-slave) flipflops

## Slide 5: Our Implementation
An edge-triggered methodology, typical execution
  read contents of some state elements (combinational activity, so no clock control signal needed)
  send values through some combinational logic
  write results to one or more state elements on clock edge
State
element
1
State
element
2
Combinational
logic
clock
one clock cycle
Assumes state elements are written on every clock cycle; if not, need explicit write control signal
  write occurs only when both the write control is asserted and the clock edge occurs

## Slide 6: Fetching Instructions
Fetching instructions involves
  reading the instruction from the Instruction Memory
  updating the PC value to be the address of the next (sequential) instruction
Read
Address
Instruction
Instruction
Memory
Add
PC
4
  PC is updated at the end of every clock cycle, so it does not need an explicit write control signal just a clock signal
  Reading from the Instruction Memory is a combinational activity, so it doesn’t need an explicit read control signal
Fetch
PC = PC+4
Decode
Exec

## Slide 7: Decoding Instructions
Decoding instructions involves
  sending the fetched instruction’s opcode and function field bits to the control unit
  and
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
Control
Unit
  reading two values from the Register File
    Register File addresses are contained in the instruction just fetched from the Instruction Memory
Fetch
PC = PC+4
Decode
Exec

## Slide 8: Reading Registers “Just in Case”
Note that both RegFile read ports are active for all instructions during the Decode cycle using the rs and rt instruction field addresses
  Since haven’t decoded the instruction yet, don’t know what the instruction is !
  Just in case the instruction uses values from the RegFile do “work ahead” by reading the two source operands
Which instructions do make use of the RegFile values?
Also, all instructions (except j) use the ALU after reading the registers
Why? memory-reference? arithmetic? control flow?
Notes: memory reference use ALU to compute addresses
arithmetic use the ALU to do the require arithmetic
control use the ALU to compute branch conditions.

## Slide 9: Executing R Format Operations
R format operations (add, sub, slt, and, or)
  perform operation (op and funct) on values in rs and rt
  store the result back into the Register File (into location rd)
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
R-type:
31
25
20
15
5
0
op
rs
rt
rd
funct
shamt
10
  Note that Register File is not written every cycle (e.g. sw), so we need an explicit write control signal for the Register File
Fetch
PC = PC+4
Decode
Exec

## Slide 10: Consider the slt Instruction
Remember the R format instruction slt
slt $t0, $s0, $s1 # if $s0 < $s1 # then $t0 = 1 # else $t0 = 0
2
  Where does the 1 (or 0) come from to store into $t0 in the Register File at the end of the execute cycle?
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite

## Slide 11: Executing Load and Store Operations
Load and store operations have to
  compute a memory address by adding the base register (in rs) to the 16-bit signed offset field in the instruction
    base register was read from the Register File during decode
    offset value in the low order 16 bits of the instruction must be sign extended to create a 32-bit signed value
  store value, read from the Register File during decode, must be written to the Data Memory
  load value, read from the Data Memory, must be stored in the Register File
I-Type:
op
rs
rt
address offset
31
25
20
15
0

## Slide 12: Executing Load and Store Operations, con’t
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
Sign
Extend
MemWrite
MemRead
Notes: For class handout

## Slide 13: Executing Load and Store Operations, con’t
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
Sign
Extend
MemWrite
MemRead
16
32
Notes: For lecture

## Slide 14: Executing Branch Operations
Branch operations have to
  compare the operands read from the Register File during decode (rs and rt values) for equality (zero ALU output)
  compute the branch target address by adding the updated PC to the sign extended16-bit signed offset field in the instruction
    “base register” is the updated PC
    offset value in the low order 16 bits of the instruction must be sign extended to create a 32-bit signed value and then shifted left 2 bits to turn it into a word address
I-Type:
op
rs
rt
address offset
31
25
20
15
0

## Slide 15: Executing Branch Operations, con’t
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
zero
ALU control
Sign
Extend
16
32
Shift
left 2
Add
4
Add
PC
Branch
target
address
(to branch control logic)
Notes: For class handout

## Slide 16: Executing Branch Operations, con’t
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
zero
ALU control
Sign
Extend
16
32
Shift
left 2
Add
4
Add
PC
Branch
target
address
(to branch control logic)
Notes: For lecture

## Slide 17: Executing Jump Operations
Jump operations have to
  replace the lower 28 bits of the PC with the lower 26 bits of the fetched instruction shifted left by 2 bits
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Shift
left 2
Jump
address
26
4
28
J-Type:
op
31
25
0
jump target address

## Slide 18: Creating a Single Datapath from the Parts
Assemble the datapath elements, add control lines as needed, and design the control path
Fetch, decode and execute each instructions in one clock cycle – single cycle design
  no datapath resource can be used more than once per instruction, so some must be duplicated (e.g., why we have a separate Instruction Memory and Data Memory)
  to share datapath elements between two different instruction classes will need multiplexors at the input of the shared elements with control lines to do the selection
Cycle time is determined by length of the longest path

## Slide 19: Fetch, R, and Memory Access Portions
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32

## Slide 20: Multiplexer Insertion
MemtoReg
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
ALUSrc

## Slide 21: Clock Distribution
MemtoReg
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
ALUSrc
System Clock
clock cycle

## Slide 22: Adding the Branch Portion
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Notes: For class handout

## Slide 23: Adding the Branch Portion
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Shift
left 2
Add
PCSrc
Notes: For lecture

## Slide 24: Our Simple Control Structure
We wait for everything to settle down
  ALU might not produce “right answer” right away
  Memory and RegFile reads are combinational (as are ALU, adders, muxes, shifter, signextender)
  Use write signals along with the clock edge to determine when to write to the sequential elements (to the PC, to the Register File and to the Data Memory)
The clock cycle time is determined by the logic delay through the longest path
We are ignoring some details like register setup and hold times

## Slide 25: Adding the Control
Selecting the operations to perform (ALU, Register File and Memory read/write)
Controlling the flow of data (multiplexor inputs)
Information comes from the 32 bits of the instruction
I-Type:
op
rs
rt
address offset
31
25
20
15
0
R-type:
31
25
20
15
5
0
op
rs
rt
rd
funct
shamt
10
Observations
  op field always in bits 31-26
  addr of two registers to be read are always specified by the rs and rt fields (bits 25-21 and 20-16)
  base register for lw and sw always in rs (bits 25-21)
  addr. of register to be written is in one of two places – in rt (bits 20-16) for lw; in rd (bits 15-11) for R-type instructions
  offset for beq, lw, and sw always in bits 15-0

## Slide 26: (Almost) Complete Single Cycle Datapath
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
ALU
ovf
zero
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Register
File
Read
Data 1
Read
Data 2
RegWrite
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
1
0
RegDst
0
1
1
0
1
0
ALU
control
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]

## Slide 27: ALU Control, Con’t
Controlling the ALU uses of multiple decoding levels
  main control unit generates the ALUOp bits
  ALU control unit generates ALUcontrol bits
Instr op | funct | ALUOp | action | ALUcontrol
lw | xxxxxx | 00 |  | 
sw | xxxxxx | 00 |  | 
beq | xxxxxx | 01 |  | 
add | 100000 | 10 | add | 0110
subt | 100010 | 10 | subtract | 1110
and | 100100 | 10 | and | 0000
or | 100101 | 10 | or | 0001
xor | 100110 | 10 | xor | 0010
nor | 100111 | 10 | nor | 0011
slt | 101010 | 10 | slt | 1111
Notes: Need 4-bit ALU control input and 2-bit ALU OP input.
2-bit ALU Op encoding: 00 (ADD for LOAD and STORE instruction), 01 SUBTRACT for branch instructions, 10 for operation encoded in the FUNCTION filed (Arithmetic and Logic operations).

## Slide 28: ALU Control, Con’t
Controlling the ALU uses of multiple decoding levels
  main control unit generates the ALUOp bits
  ALU control unit generates ALUcontrol bits
Instr op | funct | ALUOp | action | ALUcontrol
lw | xxxxxx | 00 |  | 
sw | xxxxxx | 00 |  | 
beq | xxxxxx | 01 |  | 
add | 100000 | 10 | add | 0110
subt | 100010 | 10 | subtract | 1110
and | 100100 | 10 | and | 0000
or | 100101 | 10 | or | 0001
xor | 100110 | 10 | xor | 0010
nor | 100111 | 10 | nor | 0011
slt | 101010 | 10 | slt | 1111
add | 0110
add | 0110
subtract | 1110
Notes: For lecture
Note that unsigned operations are not included. So there is no way to disable the overflow flag within the ALU. But you have have the centralized control do that, based on mo of the function field.

## Slide 29: ALU Control Truth Table
F5 | F4 | F3 | F2 | F1 | F0 | ALU Op1 | ALU Op0 | ALU control3 | ALU control2 | ALU control1 | ALU control0
X | X | X | X | X | X | 0 | 0 | 0 | 1 | 1 | 0
X | X | X | X | X | X | 0 | 1 | 1 | 1 | 1 | 0
X | X | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0
X | X | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0
X | X | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
X | X | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1
X | X | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0
X | X | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1
X | X | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1
Four, 6-input truth tables
Notes: For class handout

## Slide 30: ALU Control Truth Table
F5 | F4 | F3 | F2 | F1 | F0 | ALU Op1 | ALU Op0 | ALU control3 | ALU control2 | ALU control1 | ALU control0
X | X | X | X | X | X | 0 | 0 | 0 | 1 | 1 | 0
X | X | X | X | X | X | 0 | 1 | 1 | 1 | 1 | 0
X | X | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0
X | X | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0
X | X | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
X | X | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1
X | X | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0
X | X | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1
X | X | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1
Four, 6-input truth tables
Our ALU m control input
Add/subt
Mux control
Notes: For lecture

## Slide 31: ALU Control Logic
From the truth table can design the ALU Control logic
Instr[3]
Instr[2]
Instr[1]
Instr[0]
ALUOp1
ALUOp0
ALUcontrol3
ALUcontrol2
ALUcontrol1
ALUcontrol0
Notes: ALUcontrol3 = ALUOp0 or !F2 F1 ALUOp1
ALUcontrol2 = !F2 ALUOp1 or !ALUOp1
ALUcontrol1 = !F2 ALUOp1 or !ALUOp1 or F1 ALUOp1
ALUcontrol0 = F0 ALUOp1 or F3 ALUOp1

## Slide 32: (Almost) Complete Datapath with Control Unit
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch

## Slide 33: Main Control Unit
Instr | RegDst | ALUSrc | MemReg | RegWr | MemRd | MemWr | Branch | ALUOp
R-type 000000 |  |  |  |  |  |  |  | 
lw 100011 |  |  |  |  |  |  |  | 
sw 101011 |  |  |  |  |  |  |  | 
beq 000100 |  |  |  |  |  |  |  | 
Completely determined by the instruction opcode field
  Note that a multiplexor whose control input is 0 has a definite action, even if it is not used in performing the operation
Notes: For class handout

## Slide 34: Adding the Control
Selecting the operations to perform (ALU, Register File and Memory read/write)
Controlling the flow of data (multiplexor inputs)
Information comes from the 32 bits of the instruction
I-Type:
op
rs
rt
address offset
31
25
20
15
0
R-type:
31
25
20
15
5
0
op
rs
rt
rd
funct
shamt
10
Observations
  op field always in bits 31-26
  addr of two registers to be read are always specified by the rs and rt fields (bits 25-21 and 20-16)
  base register for lw and sw always in rs (bits 25-21)
  addr. of register to be written is in one of two places – in rt (bits 20-16) for lw; in rd (bits 15-11) for R-type instructions
  offset for beq, lw, and sw always in bits 15-0

## Slide 35: R-type Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
zero
Notes: For class handout – have a student come forward and mark the connections in the datapath that are active. And show the state of the control lines.

## Slide 36: R-type Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For lecture

## Slide 37: Store Word Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For class handout – have a student come forward and mark the connections in the datapath that are active. And show the state of the control lines.

## Slide 38: Store Word Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For lecture

## Slide 39: Load Word Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For class handout – have a student come forward and mark the connections in the datapath that are active. And show the state of the control lines.

## Slide 40: Load Word Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For lecture

## Slide 41: Branch Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For class handout – have a student come forward and mark the connections in the datapath that are active. And show the state of the control lines.

## Slide 42: Branch Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For lecture

## Slide 43: Main Control Unit
Instr | RegDst | ALUSrc | MemReg | RegWr | MemRd | MemWr | Branch | ALUOp
R-type 000000 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 10
lw 100011 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 00
sw 101011 | X | 1 | X | 0 | 0 | 1 | 0 | 00
beq 000100 | X | 0 | X | 0 | 0 | 0 | 1 | 01
Setting of the MemRd signal (for R-type, sw, beq) depends on the memory design (could be a 0 or could be a X (don’t care))
Notes: For lecture

## Slide 44: Control Unit Logic
From the truth table can design the Main Control logic
Instr[31]
Instr[30]
Instr[29]
Instr[28]
Instr[27]
Instr[26]
R-type
lw
sw
beq
RegDst
ALUSrc
MemtoReg
RegWrite
MemRead
MemWrite
Branch
ALUOp1
ALUOp0

## Slide 45: Main Control Unit
Instr | RegDst | ALUSrc | MemReg | RegWr | MemRd | MemWr | Branch | ALUOp | Jump
R-type 000000 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 10 | 0
lw 100011 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 00 | 0
sw 101011 | X | 1 | X | 0 | 0 | 1 | 0 | 00 | 0
beq 000100 | X | 0 | X | 0 | 0 | 0 | 1 | 01 | 0
j 000010 | X | X | X | 0 | 0 | 0 | X | XX | 1
Setting of the MemRd signal (for R-type, sw, beq) depends on the memory design
Notes: For class handout

## Slide 46: Additional Readings

## Slide 47: ALU Control
ALU control input | Function
0000 | and
0001 | or
0010 | xor
0011 | nor
0110 | add
1110 | subtract
1111 | set on less than
ALU's operation based on instruction type and function code
Notice that we are using different encodings than in the book

## Slide 48: State Elements
Set-reset latch
R
S
Q
!Q
R | S | Q(t+1) | !Q(t+1)
1 | 0 | 0 | 1
0 | 1 | 1 | 0
0 | 0 | Q(t) | !Q(t)
1 | 1 | 0 | 0
clock
D
Q
!Q
clock
D
Q
Level sensitive D latch
  latch is transparent when clock is high (copies input to output)

## Slide 49: Two-Sided Clock Constraint
Race problem with latch based design …
D
clock
Q
!Q
D-latch0
D
clock
Q
!Q
D-latch1
clock
Consider the case when D-latch0 holds a 0 and D-latch1 holds a 1 and you want to transfer the contents of D-latch0 to D-latch1 and vice-versa
  must have the clock high long enough for the transfer to take place
  must not leave the clock high so long that the transferred data is copied back into the original latch
Two-sided clock constraint

## Slide 50: State Elements
Solution is to use flipflops that change state (Q) only on a clock edge (master-slave)
  master (first D-latch) copies the input when the clock is high (the slave (second D-latch) is locked in its memory state and the output does not change)
  slave copies the master when the clock goes low (the master is now locked in its memory state so changes at the input are not loaded into the master D-latch)
D
clock
Q
!Q
D-latch
D
clock
Q
!Q
D-latch
Q
!Q
D
clock
clock
D
Q
Notes: Also have set-up and hold-times to deal with

## Slide 51: One-Sided Clock Constraint
Edge-triggered (master-slave) flipflops remove one of the clock constraints
D
clock
Q
!Q
MS-ff0
D
clock
Q
!Q
MS-ff1
clock
Consider the case when MS-ff0 holds a 0 and MS-ff1 holds a 1 and you want to transfer the contents of MS-ff0 to MS-ff1 and vice-versa
  must have the clock cycle time long enough to accommodate the worst case delay path
One-sided clock constraint

## Slide 52: Latches vs Flipflops
Output is equal to the stored value inside the element
Change of state (value) is based on the clock
  Latches: output changes whenever the inputs change and the clock is asserted (level sensitive methodology)
    Two-sided timing constraint
  Flip-flop: output changes only on a clock edge (edge-triggered methodology)
    One-sided timing constraint
A clocking methodology defines when signals can be read and written – wouldn’t want to read a signal at the same time it was being written