## Slide 1: CSE 424 Computer Architecture Memory Hierarchy (Caches)
Adwait Jog (http://adwaitjog.github.io/)
Based on the slides from Mary. J. Irwin (Penn State)
[Adapted from Computer Organization and Design,
5th Edition, Patterson & Hennessy,
Morgan Kaufmann]

## Slide 2: Major Components of a Computer
Processor
Control
Datapath
Memory
Devices
Input
Output
Registers
Data-centric view:
Transformations Storage Communication
The “Flat Memory” model – all accesses to Memory from the Processor take the same amount of time. It therefore doesn’t matter where you put your data.
This hasn’t been true for many years. It was once a pretty good approximation of reality, and it is still always the easiest abstraction.
Notes: PH Sec. 5.1

## Slide 3: Major Components of a Computer
Processor
Control
Datapath
Memory
Devices
Input
Output
Cache
Main Memory
Secondary Memory
Registers
Data-centric view:
Transformations Storage Communication
Disk
DRAM
SRAM
The “Hierarchical Memory” model – accesses to Memory from the Processor may take vastly different amounts of time. It therefore does matter where you put your data.
Notes: PH Sec. 5.1
Memory Hierarchy –
cache - small, fast, expensive per bit
main memory – larger, slower, cheap per bit
disk – even larger, slower, cheaper per bit
Should add additional levels or more detail for some systems –
cache (on-chip) – L1, L2, L3, local per core, or shared among cores
main memory – local per processor, shared among processors
solid-state disk (flash) –
rotating magnetic disk –

## Slide 4: Major Components of a Computer
Processor
Control
Datapath
Memory
Devices
Input
Output
L2 Cache
Main Memory
Secondary Memory
(Disk)
Secondary Memory
(Flash)
L3 Cache
L1 Cache
Registers
Data-centric view:
Transformations Storage Communication
Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts:
1. The input devices bring the data from the outside world into the computer.
2. These data are kept in the computer’s memory until ...
3. The datapath request and process them.
4. The operation of the datapath is controlled by the computer’s controller.
All the work done by the computer will NOT do us any good unless we can get the data back to the outside world.
5. Getting the data back to the outside world is the job of the output devices.
The most COMMON way to connect these 5 components together is to use a network of busses.
Workstation Design Target: 25% of cost on Processor, 25% of cost on Memory (minimum memory size), rest on I/O devices, power supplies, box

## Slide 5: Visualizing Access Times
A typical machine: (e.g., Intel Core 2 Duo, 3.0 GHz)
Level | L1 cache | L2 cache | DRAM | Disk
seconds | 1 ns | 4.7 ns | ~ 83 ns | 13.7 ms
cycles | 3 | 14 | ~ 250 | 41 million
“To put this into perspective, reading from L1 cache is like grabbing a piece of paper from your desk (3 seconds), L2 cache is picking up a book from a nearby shelf (14 seconds), and main system memory is taking a X-minute walk down the hall to buy coffee”
“Keeping with the office analogy, waiting for a hard drive seek is like leaving the building to roam the earth for one year and three months.”
http://duartes.org/gustavo/blog/post/what-your-computer-does-while-you-wait (Nov. 2008)
Notes: Disk access time is average seek time only, not counting transfer time, or a hit in the disk drive’s cache.
Compare to table on PH p. 453, for SRAM, DRAM, Magnetic Disk.

## Slide 6: How is the Memory Hierarchy Managed?
registers  memory (in the flat memory model)
  by the programmer, usually via a compiler
registers  cache  main memory
  by the cache controller hardware
main memory  secondary memory (flash, disk)
  by the operating system (virtual memory)
    virtual address to physical address mapping
    assisted by the hardware (TLB, page tables)
  by the programmer with OS support (files)
Notes: PH Sec. 5.2
More about virtual memory later.
Note which steps do not involve direct programmer intervention.

## Slide 7: Memory Hierarchy Technologies
Caches use SRAM (Static Random Access Memory) for speed and technology compatibility
  Fast (access times of 0.5 to 2.5 nsec) but low density (6 transistor cells), high power, expensive ($500 to $1000 per GiB in 2012)
  Static: content will last “forever” (as long as power is left on)
Main Memory uses DRAM (Dynamic RAM) for size
  Higher density (1 transistor cells), lower power, cheaper ($10 to $20 per GiB in 2012) but slower (access times of 50 to 70 nsec)
  Dynamic: needs to be “refreshed” regularly (~ every 8 ms)
    that consumes 1% to 2% of the active cycles of the DRAM
Secondary Memory is nonvolatile (it retains information even when the power is turned off)
  Extremely high density, cheap but access time is slow and varies from location to location and from time to time
Notes: Size comparison: DRAM/SRAM is 4 to 8 times
Cost/cycle time comparison SRAM/DRAM is 8 to 16 times

## Slide 8: Memory Hierarchy Technologies
Secondary memory uses magnetic disk for size and cost
  Much, much slower (typical access time 5 msec – 20 msec)
  Much, much lower cost ($0.05 – $.10 per GiB)
  Non-volatile
  more details later …
Flash memory currently is used as an intermediary between main (DRAM) memory and disk, or as a substitute for disk
  5,000 -50,000 ns access time, $0.75 -$ 1.0 per GiB in 2012)
Tertiary memory traditionally has used magnetic tape for size and cost
  Much3 slower
  Used for disk backups and longer-term off-site archival storage
Notes: PH Sec. 5.1, data from table on p. 453.

## Slide 9: Processor-Memory Performance Gap
“Moore’s Law”
µProc
55%/year
(2X/1.5yr)
DRAM
7%/year
(2X/10yrs)
Processor-Memory
Performance Gap (grows 50%/year)
Notes: [Fall 2008] HIDDEN SLIDE – KEEP?
[Spring, Fall 2009] open
Memory baseline is a 64KB DRAM in 1980, with three years to the next generation until 1996 and then two years thereafter with a 7% per year performance improvement in latency.
Processor assumes a 35% improvement per year until 1986, then a 55% until 2003, then 5%
Need to supply an instruction and a data item every clock cycle
In 1980 there were no caches (and no need for them), by 1995 most systems had 2 level caches (e.g., 60% of the transistors on the Alpha 21164 were in the cache)
DRAM improvements mostly went to capacity, not to speed.

## Slide 10: Growth in Processor Performance (SPECint)
Technology driven
Technology + advancements in architectures
Limits on power, available ILP, memory latencies
Notes: From 1980 to 2000 – performance was seven times faster than what would have been possible with just technology (including improved circuit design) – due to architectural innovations

## Slide 11: The “Memory Wall”
Processor vs DRAM speed disparity continues to grow
Clocks per instruction
Clocks per DRAM access
Good memory hierarchy design (esp. cache) is now essential to overall performance

## Slide 12: The Memory Hierarchy Goal
Facts of life as we know it today
  Large memories are cheap but slow
  Fast memories are expensive hence small to reduce cost
    cheap or expensive per bit
    slow or fast access times
    large or small quantities of bytes per access request
  There is a range of technologies to choose from
    on-chip: SRAM, embedded DRAM
    off-chip: DRAM, Flash, magnetic disk (internal)
    Removable: Flash, magnetic disk (external), optical disk
    Networked: file servers (near), web servers (distant)
Notes: PH Sec. 5.1
Flash memory is discussed in PH Sec. 6.4, as a disk replacement.

## Slide 13: The Memory Hierarchy Goal
How do we create a memory system that gives the illusion of being large, cheap and fast (most of the time)?
  With hierarchy
    try the fast parts first
    most of the time, this works well
    if not, move the data so it works well the next time
  With parallelism
    use multiple identical parts operating simultaneously
    for large quantities of data, this works well
  Example – keep a subset of the data in fast memory
  Example – 1-byte-wide memory  4 × 1-byte-wide memory  4-byte-wide memory
    load word takes 4 memory cycles vs. 1 memory cycle
Notes: PH Sec. 5.1
Flash memory is discussed in PH Sec. 6.4, as a disk replacement.

## Slide 14: The Memory Hierarchy
L1$ (SRAM)
L2$ (SRAM)
Main Memory (DRAM)
Secondary Memory (Disks)
Increasing distance from the processor in access time
Processor
(Relative) size of the memory at each level
Inclusive– what is in L1$ is a subset of what is in L2$ is a subset of what is in MM that is a subset of is in SM
4-8 bytes (word)
1 to 4 blocks
1,024+ bytes (disk sector = page)
8-32 bytes (block)
Take advantage of the principle of locality to present the user with as much memory as is available in the cheapest technology at the speed offered by the fastest technology
Notes: Because the upper level is smaller and built using faster memory parts, its hit time will be much smaller than the time to access the next level in the hierarchy (which is the major component of the miss penalty).

## Slide 15: A Typical Memory Hierarchy
Second
Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
ITLB
DTLB
eDRAM
Speed (%cycles): ½’s 1’s 10’s 100’s 1,000’s
Size (bytes): 100’s K’s 10K’s M’s G’s to T’s
Cost: highest lowest
By taking advantage of the principle of locality
  Can present the user with as much memory as is available in the cheapest technology
  at the speed offered by the fastest technology
Notes: Instead, the memory system of a modern computer consists of a series of black boxes ranging from the fastest to the slowest.
Besides variation in speed, these boxes also varies in size (smallest to biggest) and cost.
What makes this kind of arrangement work is one of the most important principle in computer design. The principle of locality. The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in detail in the next lectures on caches).

## Slide 16: Cache Design
Caches use SRAM for speed and technology compatibility
  Low density (6 transistor cells), high power, expensive, fast
  Static: content will last “forever” (until power turned off)
Example: A (2M X 16 bit) SRAM logic
Dout[15-0]
SRAM
2M x 16
Din[15-0]
Address
Chip select
Output enable
Write enable
16
16
21
Notes: Size comparison: DRAM/SRAM is 4 to 8 times
Cost/cycle time comparison SRAM/DRAM is 8 to 16 times
Need output enable on SRAM because outputs are tri-stated (0, 1, high impedance)

## Slide 17: Classical SRAM Organization (~Square)
r
o
w
d
e
c
o
d
e
r
row
address
4-bit data word
SRAM Cell
Array
word (row) select line
bit (data) lines
Each intersection represents a
6-T SRAM cell
Column Selector &
I/O Circuits
column
address
One memory row holds a block of data, so the column address selects the requested word from that block
Notes: Put multiple words in one memory row – splits the decoder into two decoders (row and column) and makes the memory core square reducing the length of the bit lines (but increasing the length of the word lines). The lsb part of the address goes into the column decoder (e.g., 6 bits so that 64 words are assigned to one row (with 32 bits per word gives 2**11 bit line pairs) leaving 14 bits for the row decoder (giving 2**14 word lines) for an not quite square array. This scheme is good only for up to 64 Kb to 256 Kb. For bigger memories it is too SLOW because the word and bit lines are too long.
SRAM allows you to read an entire row out at a time at a word.
Each row control line is referred to as the word line and each vertical data line is referred to as the bit line.

## Slide 18: How is the Hierarchy Managed?
registers  memory
  by the compiler (programmer?)
cache  main memory
  by the cache controller hardware
main memory  disks
  by the operating system (virtual memory)
  virtual to physical address mapping assisted by the hardware (TLB)
  by the programmer (files)

## Slide 19: The Memory Hierarchy: Why Does it Work?
Temporal Locality (locality in time)
  If a memory location is referenced then it will tend to be referenced again soon
   Keep most recently accessed data items closer to the processor
Spatial Locality (locality in space)
  If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon
   Move blocks consisting of contiguous words closer to the processor
Notes: How does the memory hierarchy work? Well it is rather simple, at least in principle.
In order to take advantage of the temporal locality, that is the locality in time, the memory hierarchy will keep those more recently accessed data items closer to the processor because chances are (points to the principle), the processor will access them again soon.
In order to take advantage of the spatial locality, not ONLY do we move the item that has just been accessed to the upper level, but we ALSO move the data items that are adjacent to it.
+1 = 15 min. (X:55)

## Slide 20: The Memory Hierarchy
L1$ (SRAM)
L2$ (SRAM)
Main Memory (DRAM)
Secondary Memory (Disks)
Increasing distance from the processor in access time
Processor
(Relative) size of the memory at each level
Inclusive– what is in L1$ is a subset of what is in L2$ is a subset of what is in MM that is a subset of is in SM
4-8 bytes (word)
1 to 4 blocks
1,024+ bytes (disk sector = page)
8-32 bytes (block)
Take advantage of the principle of locality to present the user with as much memory as is available in the cheapest technology at the speed offered by the fastest technology
Notes: Because the upper level is smaller and built using faster memory parts, its hit time will be much smaller than the time to access the next level in the hierarchy (which is the major component of the miss penalty).

## Slide 21: A Typical Memory Hierarchy
Second
Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
ITLB
DTLB
eDRAM
Speed (%cycles): ½’s 1’s 10’s 100’s 1,000’s
Size (bytes): 100’s K’s 10K’s M’s G’s to T’s
Cost: highest lowest
By taking advantage of the principle of locality
  Can present the user with as much memory as is available in the cheapest technology
  at the speed offered by the fastest technology
Notes: Instead, the memory system of a modern computer consists of a series of black boxes ranging from the fastest to the slowest.
Besides variation in speed, these boxes also varies in size (smallest to biggest) and cost.
What makes this kind of arrangement work is one of the most important principle in computer design. The principle of locality. The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in detail in the next lectures on caches).

## Slide 22: The Memory Hierarchy: Terminology
Block (aka line): the minimum unit of information that is present (or not) in a cache
Hit Rate: the fraction of memory accesses found in a level of the memory hierarchy
  Hit Time: Time to access that level which consists of
    Time to access the block + Time to determine hit/miss
Miss Rate: the fraction of memory accesses not found in a level of the memory hierarchy  1 - (Hit Rate)
  Miss Penalty: Time to replace a block in that level with the corresponding block from a lower level which consists of
    Time to access the block in the lower level + Time to transmit that block to the level that experienced the miss + Time to insert the block in that level + Time to pass the block to the requestor
Hit Time << Miss Penalty
Notes: A HIT is when the data the processor wants to access is found in the upper level (Blk X).
The fraction of the memory access that are HIT is defined as HIT rate.
HIT Time is the time to access the Upper Level where the data is found (X). It consists of:
(a) Time to access this level.
(b) AND the time to determine if this is a Hit or Miss.
If the data the processor wants cannot be found in the Upper level. Then we have a miss and we need to retrieve the data (Blk Y) from the lower level.
By definition (definition of Hit: Fraction), the miss rate is just 1 minus the hit rate.
This miss penalty also consists of two parts:
(a) The time it takes to replace a block (Blk Y to BlkX) in the upper level.
(b) And then the time it takes to deliver this new block to the processor.
It is very important that your Hit Time to be much much smaller than your miss penalty. Otherwise, there will be no reason to build a memory hierarchy.

## Slide 23: Cache Basics
Two questions to answer (in hardware):
  Q1: How do we know if a data item is in the cache?
  Q2: If it is, how do we find it?
Direct mapped
  Each memory block is mapped to exactly one block in the cache
    lots of memory blocks must share the same cache block
  Address mapping (to answer Q2):
  (memory block address) modulo (# of blocks in the cache)
  Have a tag associated with each cache block that contains the address information (the upper portion of the address) required to identify the memory block (to answer Q1)

## Slide 24: Caching: A Simple First Example
00
01
10
11
Cache
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Main Memory
Tag
Data
Q1: Is it there?
Compare the cache tag to the high order 2 memory address bits to tell if the memory block is in the cache
Valid
One word blocks
Two low order bits define the byte in the word (32b words)
Q2: How do we find it?
Use next 2 low order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
(block address) modulo (# of blocks in the cache)
Index
Notes: For class handout

## Slide 25: Caching: A Simple First Example
00
01
10
11
Cache
Main Memory
Q2: How do we find it?
Use next 2 low order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
Tag
Data
Q1: Is it there?
Compare the cache tag to the high order 2 memory address bits to tell if the memory block is in the cache
Valid
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
One word blocks
Two low order bits define the byte in the word (32b words)
(block address) modulo (# of blocks in the cache)
Index
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block

## Slide 26: Direct Mapped Cache
0
1
2
3
4
3
4
15
Consider the main memory word reference string
  0 1 2 3 4 3 4 15
Start with an empty cache - all blocks initially marked as not valid
Notes: For class handout

## Slide 27: Direct Mapped Cache
0
1
2
3
4
3
4
15
Consider the main memory word reference string
  0 1 2 3 4 3 4 15
00 Mem(0)
00 Mem(0)
00 Mem(1)
00 Mem(0)
00 Mem(0)
00 Mem(1)
00 Mem(2)
miss
miss
miss
miss
miss
miss
hit
hit
00 Mem(0)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01
4
11
15
00 Mem(1)
00 Mem(2)
00 Mem(3)
Start with an empty cache - all blocks initially marked as not valid
  8 requests, 6 misses
Notes: For lecture
Reference string is word addresses (or block number since we are using one word blocks) – i.e., the low order two bits used to selected the byte in the 32-bit word are ignored

## Slide 28: MIPS Direct Mapped Cache Example
One word blocks, cache size = 1K words (or 4KB)
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
What kind of locality are we taking advantage of?
20
Data
32
Hit
  32bit address from the PC (Instr Fetch) or ALU (load, store addr)
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
Temporal!

## Slide 29: Cache Field Sizes
The number of bits in a cache includes both the storage for data and for the tags
  32-bit byte address
  For a direct mapped cache with 2n blocks, n bits are used for the index
  For a block size of 2m words (2m+2 bytes), m bits are used to address the word within the block and 2 bits are used to address the byte within the word
What is the size of the tag field?
The total number of bits in a direct-mapped cache is then
  2n x (block size + tag field size + valid field size)
How many total bits are required for a direct mapped cache with 16KB of data and 4-word blocks assuming a 32-bit address?
Notes: The tag field is 32 – (n+m+2)
16KB is 4K (2^12 words). With a block size of 4 words, there are 1024 (2^10) blocks. Each block has 4x32 or 128 bits of data plus a tag which is 32 – 10 -2 – 2 bits, plus a valid bit. So the total cache size is
2^10 x (4x32 +18 + 1) = 2^10 x 147 = 147Kbits (or about 1.15 times as many as needed just for storage of the data).

## Slide 30: Handling Cache Hits
Read hits (L1I$ and L1D$)
  this is what we want!
Write hits (L1D$ only)
  require the cache and memory to be consistent
    always write the data into both the cache block and the next level in the memory hierarchy (write-through)
    writes run at the speed of the next level in the memory hierarchy – so slow! – or can use a write buffer and stall only if the write buffer is full
  allow cache and memory to be inconsistent
    write the data only into the cache block (write-back the cache block to the next level in the memory hierarchy when that cache block is “evicted”)
    need a dirty bit for each data cache block to tell if it needs to be written back to memory when it is evicted – can use a write buffer to help “buffer” write-backs of dirty blocks
Notes: In a write-back cache, because we cannot overwrite the block (since we may not have a backup copy anywhere), stores either require two cycles (one to check for a hit, followed by one to actually do the write) or require a write buffer to hold that data (essentially pipelining the write).
By comparison, a write-through cache can always be done in one cycle assuming there is room in the write buffer. Read the tag and write the data in parallel. If the tag doesn’t match, the generate a write miss to fetch the rest of that block from the next level in the hierarchy (and update the tag field).

## Slide 31: Sources of Cache Misses
Compulsory (cold start or process migration, first reference):
  First access to a block, “cold” fact of life, not a whole lot you can do about it. If you are going to run “millions” of instruction, compulsory misses are insignificant
  Solution: increase block size (increases miss penalty; very large blocks could increase miss rate)
Capacity:
  Cache cannot contain all blocks accessed by the program (its working set size)
  Solution: increase cache size (may increase access time)
Conflict (collision):
  Multiple memory locations mapped to the same cache location
  Solution 1: increase cache size
  Solution 2: increase associativity (may increase access time)
Notes: (Capacity miss) That is the cache misses are due to the fact that the cache is simply not large enough to contain all the blocks that are accessed by the program.
The solution to reduce the Capacity miss rate is simple: increase the cache size.
Here is a summary of other types of cache miss we talked about.
First is the Compulsory misses. These are the misses that we cannot avoid. They are caused when we first start the program.
Then we talked about the conflict misses. They are the misses that caused by multiple memory locations being mapped to the same cache location.
There are two solutions to reduce conflict misses. The first one is, once again, increase the cache size. The second one is to increase the associativity.
For example, say using a 2-way set associative cache instead of directed mapped cache.
But keep in mind that cache miss rate is only one part of the equation. You also have to worry about cache access time and miss penalty. Do NOT optimize miss rate alone.
Finally, there is another source of cache miss we will not cover today. Those are referred to as invalidation misses caused by another process, such as IO , update the main memory so you have to flush the cache to avoid inconsistency between memory and cache.
+2 = 43 min. (Y:23)

## Slide 32: Taking Advantage of Spatial Locality
0
Let cache block hold more than one word
  0 1 2 3 4 3 4 15
1
2
3
4
3
4
15
Start with an empty cache - all blocks initially marked as not valid
Notes: For class handout

## Slide 33: Taking Advantage of Spatial Locality
0
Let cache block hold more than one word
  0 1 2 3 4 3 4 15
1
2
3
4
3
4
15
00 Mem(1) Mem(0)
miss
00 Mem(1) Mem(0)
hit
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
miss
hit
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
miss
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
01
5
4
hit
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
hit
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
miss
11
15
14
Start with an empty cache - all blocks initially marked as not valid
  8 requests, 4 misses
Notes: For lecture
Show the 4-bit address mapping – 2-bits of tag, 1-bit of set address (index), 1-bit of word-in-block select

## Slide 34: Multiword Block Direct Mapped Cache
8
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
32
Block offset
Four words/block, cache size = 1K words
What kind of locality are we taking advantage of?
Notes: to take advantage for spatial locality want a cache block that is larger than word word in size.
Talk about the total number of bits for a direct-mapped cache.
Let the cache has 2^n blocks.
Then the total number of bits = 2^n (block size + Tag Size + Valid bit)

## Slide 35: Miss Rate vs Block Size vs Cache Size
Chart: Block size (bytes)
| 16.0 | 32.0 | 64.0 | 128.0 | 256.0
8 KB | 8.5 | 7.5 | 7.25 | 7.75 | 9.5
16 KB | 4 | 2.75 | 2.75 | 3 | 3.5
64 KB | 2 | 1.7 | 1.55 | 1.4 | 1.4
256 KB | 1 | 0.7 | 0.5 | 0.5 | 0.6
Miss rate goes up if the block size becomes a significant fraction of the cache size because the number of blocks that can be held in the same size cache is smaller (increasing capacity misses)
Notes: Increasing the block size usually decreases the miss rate.
A more serious problem is that the miss penalty goes up since it is primarily determined by the time to fetch the block from the next lower level of the hierarchy and load it into the cache.

## Slide 36: Block Size Tradeoff
  Larger block size means larger miss penalty
    Latency to first word in block + transfer time for remaining words
Miss
Penalty
Block Size
Miss
Rate
Exploits Spatial Locality
Fewer blocks
compromises
Temporal Locality
Block Size
Average
Access
Time
Increased Miss Penalty
& Miss Rate
Block Size
In general, Average Memory Access Time
  = Hit Time + Miss Penalty x Miss Rate
Larger block sizes take advantage of spatial locality but
  If the block size is too big relative to the cache size, the miss rate will go up
Notes: As I said earlier, block size is a tradeoff. In general, larger block size will reduce the miss rate because it take advantage of spatial locality.
But remember, miss rate NOT the only cache performance metrics. You also have to worry about miss penalty.
As you increase the block size, your miss penalty will go up because as the block gets larger, it will take you longer to fill up the block.
Even if you look at miss rate by itself, which you should NOT, bigger block size does not always win. As you increase the block size, assuming keeping cache size constant, your miss rate will drop off rapidly at the beginning due to spatial locality.
However, once you pass certain point, your miss rate actually goes up.
As a result of these two curves, the Average Access Time (point to equation), which is really the more important performance metric than the miss rate, will go down initially because the miss rate is dropping much faster than the increase in miss penalty.
But eventually, as you keep on increasing the block size, the average access time can go up rapidly because not only is the miss penalty is increasing, the miss rate is increasing as well.

## Slide 37: Other Ways to Reduce Cache Miss Rates
Allow more flexible block placement
  In a direct mapped cache a memory block maps to exactly one cache block
  At the other extreme, could allow a memory block to be mapped to any cache block – fully associative cache
  A compromise is to divide the cache into sets each of which consists of n “ways” – n-way set associative cache
Use multiple levels of caches
  Add a second level of caches on chip – normally a unified L2 cache (it holds both instructions and data)
    L1 caches focuses on minimizing hit time in support of a faster clock cycle (so smaller with smaller block sizes)
    L2 cache focuses on reducing miss rate to reduce the penalty of long main memory access times (so larger with larger block sizes)

## Slide 38: Reducing Cache Miss Rates #1
Allow more flexible block placement
In a direct mapped cache a memory block maps to exactly one cache block
At the other extreme, could allow a memory block to be mapped to any cache block – fully associative cache
A compromise is to divide the cache into sets each of which consists of n “ways” (n-way set associative). A memory block maps to a unique set (specified by the index field) and can be placed in any way of that set (so there are n choices)
  (block address) modulo (# sets in the cache)

## Slide 39: Set Associative Cache Example
0
Cache
Main Memory
Q2: How do we find it?
Use next 1 low order memory address bit to determine which cache set (i.e., modulo the number of sets in the cache)
Tag
Data
Q1: Is it there?
Compare all the cache tags in the set to the high order 3 memory address bits to tell if the memory block is in the cache
V
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Two low order bits define the byte in the word (32-b words)
One word blocks
Set
1
0
1
Way
0
1
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block

## Slide 40: Another Reference String Mapping
0
4
0
4
0
4
0
4
Consider the main memory word reference string
  0 4 0 4 0 4 0 4
Start with an empty cache - all blocks initially marked as not valid
Notes: For class handout

## Slide 41: Another Reference String Mapping
0
4
0
4
0
4
0
4
Consider the main memory word reference string
  0 4 0 4 0 4 0 4
miss
miss
miss
miss
miss
miss
miss
miss
00 Mem(0)
00 Mem(0)
01
4
01 Mem(4)
0
00
00 Mem(0)
01
4
00 Mem(0)
01
4
00 Mem(0)
01
4
01 Mem(4)
0
00
01 Mem(4)
0
00
Start with an empty cache - all blocks initially marked as not valid
Ping pong effect due to conflict misses - two memory blocks that map to the same cache block
  8 requests, 8 misses
Notes: For class handout

## Slide 42: Another Reference String Mapping
0
4
0
4
Consider the main memory word reference string
  0 4 0 4 0 4 0 4
Start with an empty cache - all blocks initially marked as not valid
Notes: For class handout

## Slide 43: Another Reference String Mapping
0
4
0
4
Consider the main memory word reference string
  0 4 0 4 0 4 0 4
miss
miss
hit
hit
000 Mem(0)
000 Mem(0)
Start with an empty cache - all blocks initially marked as not valid
010 Mem(4)
010 Mem(4)
000 Mem(0)
000 Mem(0)
010 Mem(4)
Solves the ping pong effect in a direct mapped cache due to conflict misses since now two memory locations that map into the same cache set can co-exist!
  8 requests, 2 misses
Notes: For lecture
Another sample string to try 0 1 2 3 0 8 11 0 3

## Slide 44: Four-Way Set Associative Cache
28 = 256 sets each with four ways (each with one block)
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select
Sets = 2^8 = 256
Ways = 4
Blocks/Set = 4
Words/Block = 1
Bytes/Word = 4
Notes: This is called a 4-way set associative cache because there are four cache entries for each cache index. Essentially, you have four direct mapped cache working in parallel.
This is how it works: the cache index selects a set from the cache. The four tags in the set are compared in parallel with the upper bits of the memory address.
If no tags match the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data from the way where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 45: Range of Set Associative Caches
For a fixed size cache, each increase by a factor of two in associativity doubles the number of blocks per set (i.e., the number or ways) and halves the number of sets – decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Block offset
Byte offset
Index
Tag
Notes: For class handout

## Slide 46: Range of Set Associative Caches
For a fixed size cache, each increase by a factor of two in associativity doubles the number of blocks per set (i.e., the number or ways) and halves the number of sets – decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Block offset
Byte offset
Index
Tag
Decreasing associativity
Fully associative
(only one set)
Tag is all the bits except
block and byte offset
Direct mapped
(only one way)
Smaller tags
Increasing associativity
Selects the set
Used for tag compare
Selects the word in the block
Notes: For lecture

## Slide 47: Costs of Set Associative Caches
When a miss occurs, which way’s block do we pick for replacement?
  Least Recently Used (LRU): the block replaced is the one that has been unused for the longest time
    Must have hardware to keep track of when each way’s block was used relative to the other blocks in the set
    For 2-way set associative, takes one bit per set → set the bit when a block is referenced (and reset the other way’s bit)
N-way set associative cache costs
  N comparators (delay and area)
  MUX delay (set selection) before data is available
  Data available after set selection (and Hit/Miss decision). In a direct mapped cache, the cache block is available before the Hit/Miss decision
    So its not possible to just assume a hit and continue and recover later if it was a miss
Notes: First of all, a N-way set associative cache will need N comparators instead of just one comparator (use the right side of the diagram for direct mapped cache).
A N-way set associative cache will also be slower than a direct mapped cache because of this extra multiplexer delay.
Finally, for a N-way set associative cache, the data will be available AFTER the hit/miss signal becomes valid because the hit/mis is needed to control the data MUX.
For a direct mapped cache, that is everything before the MUX on the right or left side, the cache block will be available BEFORE the hit/miss signal (AND gate output) because the data does not have to go through the comparator.
This can be an important consideration because the processor can now go ahead and use the data without knowing if it is a Hit or Miss. Just assume it is a hit.
Since cache hit rate is in the upper 90% range, you will be ahead of the game 90% of the time and for those 10% of the time that you are wrong, just make sure you can recover.
You cannot play this speculation game with a N-way set-associative cache because as I said earlier, the data will not be available to you until the hit/miss signal is valid.
+2 = 38 min. (Y:18)

## Slide 48: Benefits of Set Associative Caches
The choice of direct mapped or set associative depends on the cost of a miss versus the cost of implementation
Data from Hennessy & Patterson, Computer Architecture, 2003
Largest gains are in going from direct mapped to 2-way (20%+ reduction in miss rate)
Notes: As cache sizes grow, the relative improvement from associativity increases only slightly; since the overall miss rate of a larger cache is lower, the opportunity for improving the miss rate decreases and the absolute improvement in miss rate from associativity shrinks significantly.

## Slide 49: Review: Principle of Locality
Temporal Locality
  Keep most recently accessed data items closer to the processor
Spatial Locality
  Move blocks consisting of contiguous words to the upper levels
Hit Time << Miss Penalty
  Hit: data appears in some block in the upper level (Blk X)
    Hit Rate: the fraction of accesses found in the upper level
    Hit Time: RAM access time + Time to determine hit/miss
  Miss: data needs to be retrieve from a lower level block (Blk Y)
    Miss Rate = 1 - (Hit Rate)
    Miss Penalty: Time to replace a block in the upper level with a block from the lower level + Time to deliver this block’s word to the processor
    Miss Types: Compulsory, Conflict, Capacity
Lower Level
Memory
Upper Level
Memory
To Processor
From Processor
Blk X
Blk Y

## Slide 50: Measuring Cache Performance
Assuming cache hit costs are included as part of the normal CPU execution cycle, then
  CPU time = IC × CPI × CC
  = IC × (CPIideal + Memory-stall cycles) × CC
CPIstall
Memory-stall cycles come from cache misses (a sum of read-stalls and write-stalls)
  Read-stall cycles = read miss rate × read miss penalty
  Write-stall cycles = write miss rate × write miss penalty
  + write buffer stalls
For write-through caches, we can simplify this to
  Memory-stall cycles = miss rate × miss penalty
Notes: Reasonable write buffer depth (e.g., four or more words) and a memory capable of accepting writes at a rate that significantly exceeds the average write frequency means write buffer stalls are small
Average Memory Access time = Hit Time + Miss Rate x Miss Penalty

## Slide 51: Impacts of Cache Performance
Relative cache penalty increases as processor performance improves (faster clock rate and/or lower CPI)
  The memory speed is unlikely to improve as fast as processor cycle time. When calculating CPIstall, the cache miss penalty is measured in processor clock cycles needed to handle a miss
  The lower the CPIideal, the more pronounced the impact of stalls
A processor with a CPIideal of 2, a 100 cycle miss penalty, 36% load/store instr’s, and 2% I$ and 4% D$ miss rates
  Memory-stall cycles = 2% × 100 + 36% × 4% × 100 = 3.44
  So CPIstalls = 2 + 3.44 = 5.44
What if the CPIideal is reduced to 1? 0.5? 0.25?
What if the processor clock rate is doubled (doubling the miss penalty)?
Notes: For ideal CPI = 1, then CPIstall = 4.44 and the amount of execution time spent on memory stalls would have risen from 3.44/5.44 = 63% to 3.44/4.44 = 77%
For miss penalty of 200, memory stall cycles = 2% 200 + 36% x 4% x 200 = 6.88 so that CPIstall = 8.88
This assumes that hit time is not a factor in determining cache performance. A larger cache would have a longer access time (if a lower miss rate), meaning either a slower clock cycle or more stages in the pipeline for memory access.

## Slide 52: Average Memory Access Time (AMAT)
A larger cache will have a longer access time. An increase in hit time will likely add another stage to the pipeline. At some point the increase in hit time for a larger cache will overcome the improvement in hit rate leading to a decrease in performance.
Average Memory Access Time (AMAT) is the average to access memory considering both hits and misses
  AMAT = Time for a hit + Miss rate x Miss penalty
What is the AMAT for a processor with a 20 psec clock, a miss penalty of 50 clock cycles, a miss rate of 0.02 misses per instruction and a cache access time of 1 clock cycle?
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 53: Reducing Cache Miss Rates #1
Allow more flexible block placement
In a direct mapped cache a memory block maps to exactly one cache block
At the other extreme, could allow a memory block to be mapped to any cache block – fully associative cache
A compromise is to divide the cache into sets each of which consists of n “ways” (n-way set associative). A memory block maps to a unique set (specified by the index field) and can be placed in any way of that set (so there are n choices)
  (block address) modulo (# sets in the cache)
Notes: All of the tags of all of the elements of the set must be searched for a match.

## Slide 54: Reducing Cache Miss Rates #2
Use multiple levels of caches
With advancing technology have more than enough room on the die for bigger L1 caches or for a second level of caches – normally a unified L2 cache (i.e., it holds both instructions and data) and in some cases even a unified L3 cache
For our example, CPIideal of 2, 100 cycle miss penalty (to main memory) and a 25 cycle miss penalty (to UL2$), 36% load/stores, a 2% (4%) L1I$ (L1D$) miss rate, add a 0.5% UL2$ miss rate
  CPIstalls = 2 + .02×25 + .36×.04×25 + .005×100 + .36×.005×100 = 3.54 (as compared to 5.44 with no L2$)
Notes: Also reduces cache miss penalty

## Slide 55: Multilevel Cache Design Considerations
Design considerations for L1 and L2 caches are very different
  Primary cache should focus on minimizing hit time in support of a shorter clock cycle
    Smaller with smaller block sizes
  Secondary cache(s) should focus on reducing miss rate to reduce the penalty of long main memory access times
    Larger with larger block sizes
    Higher levels of associativity
The miss penalty of the L1 cache is significantly reduced by the presence of an L2 cache – so it can be smaller (i.e., faster) but have a higher miss rate
For the L2 cache, hit time is less important than miss rate
  The L2$ hit time determines L1$’s miss penalty
  L2$ local miss rate >> than the global miss rate
Notes: Global miss rate – the fraction of references that miss in all levels of a multilevel cache. The global miss rate dictates how often we must access the main memory.
Local miss rate – the fraction of references to one level of a cache that miss

## Slide 56: Split vs Unified Caches
Split L1I$ and L1D$: instr’s and data in different caches at L1
  To minimize structural hazards and thit
    So low capacity/associativity (to reduce thit)
    So small to medium block size (to reduce conflict misses)
  To optimize L1I$ for wide output (superscalar) and no writes
Unified L2, L3, …: instr’s and data together in one cache
  To minimize %miss (thit is less important due to (hopefully) infrequent accesses)
    So high capacity/associativity/block size (to reduce %miss)
  Fewer capacity misses: unused instr capacity can be used for data
  More conflict misses: instr / data conflicts (smaller effect in large caches)
  Instr / data structural hazards are rare (would take a simultaneous L1I$ and L1D$ miss)

## Slide 57: Reducing Cache Miss Rates #3
Hardware prefetching
  Fetch blocks into the cache proactively (speculatively)
  Key is to anticipate the upcoming miss addresses accurately
  Relies on having unused memory bandwidth available
A simple case is to use next block prefetching
  Miss on address X → anticipate next reference miss on X + block-size
  Works well for instr’s (sequential execution) and for arrays of data
Need to initiate prefetches sufficiently in advance
If prefetch instr/data that is not going to be used then have polluted the cache with unnecessary data (possibly evicting useful data)

## Slide 58: Two Machines’ Cache Parameters
 | Intel Nehalem | AMD Barcelona
L1 cache organization & size | Split I$ and D$; 32KB for each per core; 64B blocks | Split I$ and D$; 64KB for each per core; 64B blocks
L1 associativity | 4-way (I), 8-way (D) set assoc.; ~LRU replacement | 2-way set assoc.; LRU replacement
L1 write policy | write-back, write-allocate | write-back, write-allocate
L2 cache organization & size | Unified; 256KB (0.25MB) per core; 64B blocks | Unified; 512KB (0.5MB) per core; 64B blocks
L2 associativity | 8-way set assoc.; ~LRU | 16-way set assoc.; ~LRU
L2 write policy | write-back | write-back
L2 write policy | write-back, write-allocate | write-back, write-allocate
L3 cache organization & size | Unified; 8192KB (8MB) shared by cores; 64B blocks | Unified; 2048KB (2MB) shared by cores; 64B blocks
L3 associativity | 16-way set assoc. | 32-way set assoc.; evict block shared by fewest cores
L3 write policy | write-back, write-allocate | write-back; write-allocate

## Slide 59: Summary: Improving Cache Performance
0. Reduce the time to hit in the cache
  smaller cache
  direct mapped cache
  smaller blocks
  for writes
    no write allocate – no “hit” on cache, just write to write buffer
    write allocate – to avoid two cycles (first check for hit, then write) pipeline writes via a delayed write buffer to cache
1. Reduce the miss rate
  bigger cache
  more flexible placement (increase associativity)
  larger blocks (16 to 64 bytes typical)
  victim cache – small buffer holding most recently discarded blocks

## Slide 60: Summary: Improving Cache Performance
2. Reduce the miss penalty
  smaller blocks
  use a write buffer to hold dirty blocks being replaced so don’t have to wait for the write to complete before reading
  check write buffer (and/or victim cache) on read miss – may get lucky
  for large blocks fetch critical word first
  use multiple cache levels – L2 cache not tied to CPU clock rate
  faster backing store/improved memory bandwidth
    wider buses
    memory interleaving, DDR SDRAMs

## Slide 61: Summary: The Cache Design Space
Several interacting dimensions
  cache size
  block size
  associativity
  replacement policy
  write-through vs write-back
  write allocation
The optimal choice is a compromise
  depends on access characteristics
    workload
    use (I-cache, D-cache, TLB)
  depends on technology / cost
Simplicity often wins
Associativity
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.

## Slide 62: Cache Summary
The Principle of Locality
  A program is likely to access a relatively small portion of the address space over a long period of time
    Temporal Locality: Locality in Time – repeated access
    Spatial Locality: Locality in Space – nearby access
Three major categories of cache misses
  Compulsory misses: sad facts of life, e.g., cold start misses
  Conflict misses: increase cache size and/or associativity
    Nightmare Scenario: ping pong effect
  Capacity misses: increase cache size
Cache design space
  total size, block size, associativity (replacement policy)
  write-hit policy (write-through, write-back)
  write-miss policy (write allocate, write buffers)
Notes: Let’s summarize today’s lecture. I know you have heard this many times and many ways but it is still worth repeating. Memory hierarchy works because of the Principle of Locality which says a program will access a relatively small portion of the address space at any instant of time. There are two types of locality: temporal locality, or locality in time and spatial locality, or locality in space.
So far, we have covered three major categories of cache misses.
Compulsory misses are cache misses due to cold start. You cannot avoid them but if you are going to run billions of instructions anyway, compulsory misses usually don’t bother you.
Conflict misses are misses caused by multiple memory location being mapped to the same cache location. The nightmare scenario is the ping pong effect when a block is read into the cache but before we have a chance to use it, it was immediately forced out by another conflict miss. You can reduce Conflict misses by either increase the cache size or increase the associativity, or both.
Finally, Capacity misses occurs when the cache is not big enough to contains all the cache blocks required by the program. You can reduce this miss rate by making the cache larger.
There are two write policy as far as cache write is concerned. Write through requires a write buffer and a nightmare scenario is when the store occurs so frequent that you saturates your write buffer.
The second write polity is write back. In this case, you only write to the cache and only when the cache block is being replaced do you write the cache block back to memory.
No fancy replacement policy is needed for the direct mapped cache. That is what caused direct mapped cache trouble to begin with – only one place to go in the cache causing conflict misses.